## Slide 1: High-Level Synthesis with Bluespec: An FPGA Designer’s Perspective
Jeff Cassidy
University of Toronto
Jan 16, 2014

## Slide 2: Disclaimer
I do applications: not an HLS expert
Have not used all tools mentioned; Sources: personal experience, reading, conversations
Opinions are my own
Discussion welcome

## Slide 3: Outline
Introduction
  Quick overview of High-Level Synthesis
  Bluespec Features
Case study: FullMonte biophotonic simulator
From Verilog to BSV
Summary

## Slide 4: Programming FPGAs is Hard!
Annual complaints at FCCM, FPGA, etc
How to fix?
  Overlay architectures
  Better CAD: P&R, latency-insensitive
  Better devices: NoC etc
  “Magic” C/Java/OpenCL/Matlab-to-gates
  Better hardware design language

## Slide 5: Software to Gates: The Problem
Inputs
Algorithm
Outputs
Functional Units
Architecture (macro, micro)
Synchronization
Layout
Semantic
Gap

## Slide 6: High-Level Synthesis
Impulse-C, Catapult-C, …-C, Vivado HLS, LegUp
Maxeler MaxJ, IBM Lime
Matlab: Xilinx System Generator, Altera DSP Builder
Altera OpenCL

## Slide 7: Can’t Have It All
Success requires specialization
  System Generator/DSP Builder: DSP apps (dataflow)
  Maxeler MaxJ: Data flow graphs from Java
  Altera OpenCL: Explicit parallelization (dataflow)
  LegUp & Vivado: Embedded acceleration

## Slide 8
OK, we know how to do dataflow…
What about control?
Memory controllers, switches, NoC, I/O…
What about hardware designers?
Notes: Legacy codebase
Existing programmers -> embedded -> multithreaded -> hardware

## Slide 9: Bluespec
  …is not:
  an imperative language
  a way for software coders to make hardware
  a way out of designing architecture
  …is:
  a productive language for hardware designers
  a quick, clean way to explore architecture
  much more concise than Verilog/VHDL

## Slide 10: Bluespec
Designing hardware
  Instantiate modules, not variables
  Aware of clocks & resets
  Anything possible in Verilog
  Fine-grained control over resources, latency, etc
Explore more microarchitectures faster
Can use same language to model & refine

## Slide 11: Bluespec : RTL :: C++ : Assembly
Low-level
  Bit-hacking
  Design as hierarchy of modules
  Bit-/Cycle-accurate simulation
  Seamless integration of legacy Verilog
  No overhead; get the h/w you ask for and no more

## Slide 12: Bluespec : RTL :: C++ : Assembly
High-level
  Concise
  Composable
  Abstraction & reuse, library development
  Correctness by design
  Fast simulation
  Helpful compiler

## Slide 13: History of Bluespec
Research at MIT CSAIL late 90’s-2000s (Prof Arvind)
Origin: Haskell (functional programming)
Semiconductor startup Sandburst 2000
  Designing 10G Ethernet routers
  Early version used internally
Bluespec Inc founded 2003

## Slide 14: Case Study: FullMonte Biophotonic Simulations

## Slide 15: Timeline
2010 Learning Haskell for personal interest
2011 Applied for MASc
First heard of Bluespec
mid-2012 receive Bluespec license, start tinkering
Implement/optimize software model
March 2013 start writing code for thesis
Sep 2013 code complete, debugged, validated
Dec 2013 Thesis defense 

## Slide 16: Case Study: My Research
Biophotonics: Interaction of light and living tissue
Clinical detection & treatment of disease
Medical research
Light scattered ~101-103 times / cm of path traveled
Simulation of light distribution crucial & compute-intensive

## Slide 17: Case Study: My Research
Bioluminescence Imaging
Tag cancer cells with bioluminescent marker
Image using low-light camera
Watch spread or remission of disease
[Left] Dogdas, Stout, et al. Digimouse: a 3D whole body mouse atlas from CT and cryosection data. Phys Med Biol 52(3) 2007.

## Slide 18: Case Study: My Research
Photodynamic Therapy (PDT) of Head & Neck Cancers
Light + Drug + Tissue Oxygen = Cell death
Need to simulate light
Heterogeneous structure
Brain
Tumour
Mandible
Spine
Larnyx
Esophagus
Courtesy R. Weersink
Princess Margaret Cancer Centre

## Slide 19: Case Study: My Research
Gold standard model
Monte Carlo ray-tracing of photon packets
  Absorption proportional, not discrete
Tetrahedral mesh geometry
Compute-intensive!
PDT: Outer loop
101-103 times
Inner loop
102-103 loops/packet
PDT Plan Total
1011-1015 loops
Launch
~108-109 packets
Notes: Over 10^16 ops!! Sine, cosine, ray-tetrahedron intersection
10s of ops per loop: 10^16+ ops!! (CPU 3e9 per sec => 10^6-10^7 seconds = hundreds of hours)

## Slide 20: Case Study: My Research
Aug-Dec 2012: FullMonte Software
Fastest MC tetrahedral mesh software available
  C++
  Multithreaded
  SIMD optimized
~30-60 min per simulation
  Not fast enough! Time to accelerate

## Slide 21: Acceleration
[Right] Dogdas, Stout, et al. Digimouse: a 3D whole body mouse atlas from CT and cryosection data. Phys Med Biol 52(3) 2007.
Infinite planar layers
FPGA: William Lo “FBM” (U of T)
GPU: CUDAMCML, GPUMCML
Voxels
GPU: MCX
Tetrahedral mesh (300k elements)
Done in software (TIM-OS)
No prior GPU or FPGA acceleration

## Slide 22: Case Study: My Research
Fully unrolled, attempts 1 hop / clock
Multiple packets in flight
  Launch to prevent hop stall
  Queue where paths merge
100% utilization of hop core
  Most DSP-intensive
  Part of all cycles in flow
Random numbers queued for use when needed
  Scattering angle (Henyey-Greenstein)
  Step lengths (exponential)
  2D/3D unit vectors
Notes: ~75% of logic/ALM is for pipeline balancing
Large packet structure

## Slide 23: Case Study: My Research
  FullMonte Hardware: First & Only Accelerated Tetrahedral MC
  TT800 Random Number Generator
  Logarithm
  CORDIC sine/cosine
  Henyey-Greenstein function
  Square-root
  3x3 Matrix multiply
  Ray-tetrahedron intersection test
  Divider
  Pipeline queuing and flow control
  Block RAM read and read-accumulate-write
4.5 KLOC BSV incl. testbenches
~6 months: learn BSV, implement, debug

## Slide 24: Results
Simulated, Validated, Place & Route (Stratix V GX A7)
Slowest block 325 MHz, system clock 215 MHz
3x faster than quad-core Sandy Bridge @ 3.6GHz
  48k tetrahedral elements
  Single pipeline; can fit 4 on Stratix V A7
  60x power efficiency vs CPU
Next Steps
Tuning
Scale up to 4 instances on one Altera Stratix V A7
Handle larger meshes using custom memory hierarchy

## Slide 25: From Verilog to Bluespec SystemVerilog

## Slide 26: From Verilog to BSV
What’s the same
Design as hierarchy of modules
Expression syntax, constants
Blocking/non-blocking assignments (but no assign stmt)
What’s different
Actions & rules
Separation of interface from module
Strong type system
Polymorphism

## Slide 27: BSV 101: Making a Register
Bluespec
Reg#(UInt#(8)) r <- mkReg(0);
rule upcount if (ctr_en);
r <= r+1;
endrule
Verilog
reg r[7:0];
always(@posedge clk)
begin
if (rst)
r <= 0;
else if(ctr_en)
r <= r+1;
end
Identical function
8 lines -> 4
Explicit state instantiation, not behavioral inference
Better clarity (less boilerplate)
Notes: Readability: it’s a reg!
Reset, clock implicit
Rule ~= always block

## Slide 28: Actions
Fundamental concept: atomic actions
Idea similar to database transaction
All-or-nothing
Can ‘fire’ only if all side effects are conflict-free
// fires only if no one else writes to a and b
action
a <= a+1;
b <= b-1;
endaction
action
a <= 0;
endaction
Conflict
Notes: Add compiler warning for conflicting actions
Mention explicit vs compiler-handled
“rule is like always block except compiler schedules for you”

## Slide 29: Rules
Rule = action + condition
Similar to always block, but far more powerful
Rule fires when:
  Explicit conditions true
  Implicit conditions true
  Effects are compatible with other active rules
Compiler generates scheduler: chooses rules each clk
Notes: Add compiler warning for conflicting actions
Mention explicit vs compiler-handled
“rule is like always block except compiler schedules for you”

## Slide 30: Rules
rule enqEveryFifth if (ctr % 5 == 0);
myFifo.enq(5);
endrule
rule enqEveryThird if (ctr % 3 == 0);
myFifo.enq(3);
endrule
Compiler says…
Warning: "FifoExample.bsv", line 26, column 8: (G0010)
Rule "enqEveryFifth" was treated as more urgent than
"enqEveryThird". Conflicts:
"enqEveryFifth" cannot fire before "enqEveryThird":
calls to myFifo.enq vs. myFifo.enq
"enqEveryThird" cannot fire before "enqEveryFifth":
calls to myFifo.enq vs. myFifo.enq
Verilog file created: mkFifoTest.v
Explicit condition
Implicit conditions:
can’t enq a full FIFO
Can only enq one thing per clock
Notes: Add compiler warning for conflicting actions
Mention explicit vs compiler-handled
“rule is like always block except compiler schedules for you”

## Slide 31: Rules
(* descending_urgency=“enqEveryFifth,enqEveryThird” *)
rule enqEveryFifth if (ctr % 5 == 0);
myFifo.enq(5);
endrule
rule enqEveryThird if (ctr % 3 == 0);
myFifo.enq(3);
endrule
Compiler says… no problem
Verilog file created: mkFifoTest2.v
Notes: Add compiler warning for conflicting actions
Mention explicit vs compiler-handled
“rule is like always block except compiler schedules for you”

## Slide 32: Rules
rule enqEvens if (ctr % 2 == 0);
myFifo.enq(ctr);
endrule
rule enqOdds if (ctr % 2 == 1);
myFifo.enq(2*ctr);
endrule
Compiler says…
Verilog file created: mkFifoTest3.v
…no problem; it can prove the rules do not conflict
Notes: Add compiler warning for conflicting actions
Mention explicit vs compiler-handled
“rule is like always block except compiler schedules for you”

## Slide 33: Rules
(* fire_when_enabled *)
rule enqStuff if (en);
myFifo.enq(val);
endrule
method Action put(UInt#(8) i);
myFifo.enq(i);
endmethod
Compiler says…
Warning: "FifoExample.bsv", line 74, column 8: (G0010)
Rule "put" was treated as more urgent than "enqStuff". Conflicts:
"put" cannot fire before "enqStuff": calls to myFifo.enq vs. myFifo.enq
"enqStuff" cannot fire before "put": calls to myFifo.enq vs. myFifo.enq
Error: "FifoExample.bsv", line 82, column 6: (G0005)
The assertion `fire_when_enabled' failed for rule `RL_enqStuff'
because it is blocked by rule
put
in the scheduler
esposito: [put -> [], RL_enqStuff -> [put], RL_val__dreg_update -> []]
Notes: Add compiler warning for conflicting actions
Mention explicit vs compiler-handled
“rule is like always block except compiler schedules for you”

## Slide 34: Methods vs Ports
Ports replaced by method calls (like OOP) – 3 types:
  Function: returns a value (no side-effects)
    Can always fire
    Ex: querying (not altering) module state: isReady, etc.
  Action: changes state; may have a condition
    May have explicit or implicit conditions
    Ex: FIFO enq
  ActionValue: action that also returns a value
    May have conditions
    Ex: Output of calculation pipeline (value may not be there yet)

## Slide 35: Methods vs Ports
Verilog
wire[7:0] val;
wire ivalid;
wire vFifo_ren, vFifo_wen;
wire vFifo_rdy;
wire[7:0] vFifo_din;
wire[7:0] vFifo_dout;
Fifo_inst#(16)(
.ren(vFifo_ren),
.wen(vFifo_wen),
.din(vFifo_din),
.dout(vFifo_dout),
.rdy(vFifo_rdy));
assign vFifo_wen = vFifo_rdy
and ivalid;
assign vFifo_val = val_in;
Wire#(Uint#(8)) val <- mkWire;
let bsvFifo <- mkSizedFIFO(16);
rule enqValueWhenValid;
bsvFifo.enq(val);
// … other stuff …
endrule
Notes: Latency-insensitive design

## Slide 36: Methods vs Ports
Method conditions are “pushed” upstream
Any action which calls a method (eg. FIFO enq) automatically gets that method’s conditions
  Implicit conditions
Conditions are formally enforced by compiler

## Slide 37: Methods vs Ports
Hardware: Compiler makes handshaking signals
  ready output (when able to fire)
  enable input (to tell it to fire)
  Can also provide can_fire, will_fire outputs for debug
Not overhead; Verilog designer must do this too!
BSV Scheduler drives ready, enable, can_fire, will_fire
BSV compiler does it for you

## Slide 38: Strong Typing
Concept inherited from Haskell
Type includes signed/unsigned, bit length
No implicit conversions; must request:
  Extend (sign-extend) / truncate
  Signed/unsigned
Can be “lazy” where type is “obvious”
let r <- myFIFO.first;

## Slide 39: Typeclasses
Arith#(t) means t implements + - * /, others…
function t add3(t a,t b,t c) provisos (Arith#(t));
return a+b+c;
Endfunction
Can define modules & functions that accept any type in a given typeclass
  Eg FIFO, Reg require Bit#(t,nb)

## Slide 40: Polymorphic Types
Maybe#(Tuple2#(t1,t2)) v; // data-valid signal
if isValid(v) ...
if (v matches tagged Valid {.v1,.v2}) ...
// can use v, v1, v2 as values here
Tuple2#(t1,t2) x =
fromMaybe(tuple2(default1,default2),v))
Notes: Should simplify out Tuple2 – demonstrating 2 concepts at same time

## Slide 41: Handy Bits
Default register (DReg)
  Resets to a default value each clk unless written to
Wire
  Physical wire with implicit data-valid signal
  Readable only if written within same clk (write-before-read)
RWire
  Like wire but returns a Maybe#(t)
  Always readable; returns Invalid if not written
  Returns Valid .v (a value) if written within same clk

## Slide 42: Handy Bits
Wire#(Uint#(16)) val_in <- mkWire;
Reg#(Uint#(32)) accum <- mkReg(0);
rule accumulate;
accum <= accum + extend(val_in);
endrule
rule foo (…);
val_in <= 10;
Endrule
method Action put(UInt#(16) i);
val_in <= I;
endmethod
Implicit condition
val_in valid only when written
Conflict
Write to same element; method will override and compiler will warn

## Slide 43: Handy Bits
Reg#(Maybe#(Int#(16)) val_in_q <- mkDReg(tagged Invalid);
Reg#(Bool) valid_d <- mkReg(False);
rule accum if (val_in_q matches tagged Valid .i);
accum <= accum + extend(i);
endrule
rule delay_ivalid_signal;
valid_d <= isValid(val_in_q);
Endrule
method Action put(Int#(16) i);
val_in_q <= i;
endmethod
Always fires (Reg always readable)
Will be tagged Invalid if not written
Will be Valid .v if written
Explicit condition

## Slide 44: Libraries
FIFOs, BRAM, Gearbox, Fixpoint, synchronizers…
Gray counter
AXI4, TLM2, AHB
Handy stuff: DReg, DWire, RWire, common interfaces…
Sequential FSM sub-language with actions
  if-then
  while-do

## Slide 45: Workflows
BSV + C  Native object file (.o) for Bluesim
  Assertions
  C testbench / modules
  Tcl-controlled interaction
  Verilog code must be replaced by BSV/C functional model
BSV + Verilog + C  Verilog + VPI  RTL Simulation
  Automatic VPI wrapper generation
BSV + Verilog  Synthesizable Verilog  Vendor synthesis
  Reasonably readable net/hierarchy identifiers

## Slide 46: Summary

## Slide 47: Strengths
Variable level of abstraction
Fast simulation (>10x over RTL w ModelSim)
Concise code
Minimal new syntax vs Verilog
Clean integration with C++
Verilog output code relatively readable

## Slide 48: Weaknesses
Some issues inferring signed multipliers (Altera S5)
  Workaround
Built-in file I/O library weak
  Wrote my own in C++ - fairly easy
Support for fixed-point, still a lot of manual effort
Can’t use Bluesim when Verilog code included
  Create functional model (BSV or C++) or use ModelSim

## Slide 49: Summary
Learned language and wrote thesis project in ~6m
Performance/area comparable to hand-coded
Much more productive than Verilog/VHDL
  Write less code
  Compiler detects more errors
  Fast simulation

## Slide 50: Summary
Great for control-intensive tasks
  Creating NoC
  Switches, routers
  Processor design
Good target for latency-insensitive techniques
Simulate quickly, then refine & explore architectures
Fast to learn - Rapid return on investment

## Slide 51: Thank You
Questions?
Free books: www.bluespec.com; U of T has s/w license
For help setting up Bluespec, just ask!
jeffrey.cassidy@gmail.com