## Slide 1: Virtualized FPGA accelerators in Cloud Computing Systems
Stuart Byma and Paul Chow
University of Toronto

## Slide 2: What is this “Cloud Computing”?
?
Not everyone seems to be on the same page with this
Notes: Term still seems to be flung around quite a bit in the business and IT world
means different things to different people

## Slide 3: What is this “Cloud Computing”?
Some fundamental characteristics
  On demand self service
    I can provision new resources at any time, without human interaction
  Rapid elasticity
    I can rapidly expand or contract the amount of resources I have – on the fly
  Resource pooling
    The provider resources are abstracted into pools, to enable serving multiple users
http://csrc.nist.gov/publications/nistpubs/800-145/SP800-145.pdf
Notes: - On Demand self service – the notion that end users can unilaterally provision resources on demand, without human interaction with the provider
- Rapid elasticity – computing or other resources can be rapidly deployed or released, automatically or otherwise. Essentially “scalability”. To the end user, the amount of resources available for provisioning appears infinite.
- Resource pooling – provider resources are abstracted into pools, to enable serving multiple users/tenants.

## Slide 4: Cloud Resources
Meaning of “resources” depends on the Service Model
Software as a Service (Google Apps)
  Provides application software, databases, support
Platform as a Service (Windows Azure)
  OS, dev and execution framework, DB, web server
Infrastructure as a Service (Amazon EC2)
  Virtual machines, storage, connectivity

## Slide 5: OpenStack – A Cloud Computing Platform
OpenStack – an open source cloud computing platform
  Enabling infrastructure as a service
  We use OpenStack as our base system (actually the SAVI Testbed, more to come …)
Notes: OpenStack – open source framework that has the above characteristics
Enables infrastructure as a service – end user available resources are virtual machines whose base pool resources are CPUs and RAM
Openstack also has other resources – object storage, volume storage, VM image management,
Question – can we include FPGAs as pooled resources? And modify OpenStack to support and manage them like VMs?

## Slide 6: The Point
We aim to “Virtualize” FPGAs, enable them as Cloud resources
How?
Well, how does OpenStack work?
  And how does it manage resources?

## Slide 7: It’s Complicated
Notes: Quick transition slide

## Slide 8: But basically:
Server
Hypervisor
Agent
VM
VM
. . .
OpenStack Controller
Resource DB
API
Notes: To keep things ridiculously simple …
User: Give me VM
OpenStack: Scheduler, find me available resource
Scheduler: (Query DB) Here is agent with resource
OpenStack: Agent, boot VM with these parameters
Agent: (Agent boots via hypervisor) OK, done.
OpenStack: User, here is VM

## Slide 9: VMs as OpenStack Cloud Resources
Virtual Machines
  Run on top of hypervisors
  One server = many VMs
    For many users
  Agent process
    Interacts with Openstack controller
    Instructs hypervisor to boot / destroy VMs
Server
Hypervisor
Agent
VM
VM
. . .
Can we do something like this for FPGAs?
Notes: How does OpenStack boot/manage VMs?
Agent process runs on physical machine beside hypervisor
User requests VM (resource) from controller, controller finds available resources in pool, contacts appropriate Agent
Agent interprets command, instructs hypervisor to boot VM with user provided OS image
Openstack returns handle to user (usually a network address)

## Slide 10: FPGAs as OpenStack Cloud Resources
FPGA
  Hypervisor? Non existent
  One FPGA = One user
  Agent? Non existent
Server
Hypervisor ??
Agent ??
FPGA ??
Notes: Compare a virtual machine as a cloud resource to an FPGA
There is no such thing as an FPGA hypervisor, therefore only one user can use one FPGA at a time
There is no agent software that supports offering FPGAs as resources to the openstack controller
Now we can think about how to enable FPGAs as an OpenStack controlled resource
  We need an agent, of some sort, that talks to OpenStack controller – and we need think about what resources agent will control
    A whole FPGA? This is not good for scalability - a lot of useful hardware accelerators don’t need a whole chip anyway
    Pieces of an FPGA? This is closer to a VM like abstraction – how? Dynamic partial reconfiguration! Hypervisor = Agent + Static Logic
  Also important – How will the FPGA resource communicate with users other resources?
    May not be in same physical machine as VM – only option is over the network

## Slide 11: FPGAs as OpenStack Cloud Resources
We want a way to make FPGAs analogous to VMs
  So they can be managed directly by OpenStack
FPGA
Agent
We need an agent
To manage the FPGA
Creating FPGA resources that the user can “boot”
With network connectivity
Notes: - We say bootable in analogy to Virtual Machines – also the OpenStack command used to get a VM or a VFR is “$nova boot”

## Slide 12: Getting there …
Single FPGA is still single user - wasteful
Relatively slow to configure
Security vulnerabilities
  Direct access to network
  User could do nasty things!
FPGA
Agent
Server

## Slide 13: Partial Reconfigurable Regions
Fix? Use PR!
Virtualized FPGA Resources
Multi-tenant
Static logic contains chip level IO, memory controllers, etc.
  Allows us to police VFR interfaces (security)
FPGA
VFR
VFR
. . .
Agent
Server

## Slide 14
Now we can “boot” a network connected FPGA accelerator on demand, in seconds!
Server
Hypervisor
Agent
VM
VM
. . .
FPGA(s)
VFR
VFR
. . .
Server
Agent
OpenStack Controller
Resource DB
API
Notes: Virtual FPGA Resources are layer 2 network devices – accessible from users VMs

## Slide 15: OpenStack Driver
How does OpenStack know how to communicate with our agent?
  We also define a Driver: an object that implements OpenStack boot, release, and general resource management API calls
OpenStack
Controller
Agent
?
Driver

## Slide 16: An Example – Consider:
A massive video web service (yootube.com?)
Running on top of ten thousand VMs
  Number of VMs can scale according to current demand
Large amount of video transcoding / compression needs to be done
  We have FPGA cloud resources now, do it in hardware
  Offload VM workload – less x86 CPUs, save power!

## Slide 17: Example
Dynamically scalable according to demand
Same OpenStack command to boot/release either resource!
VM Resource
VFR
Video Transcode/ Compress
Web Server
Site Requests
Uploads
Internal Network
x10 000
Data Center
Outside
World

## Slide 18: Boot/Release Sequence
On boot, OpenStack sends request, image(bitstream), networking information to agent via driver
Agent configures bitstream into available region, programs MAC address
  VFR is then network connected device belonging to the user
On release, agent configures black box – removes user IP, conserves power

## Slide 19: Partial Bitstream as an Image
A Virtual Machine has an operating system image
A VFR has a partial bitstream as an image
In OpenStack infrastructure, users can upload their own images
Result – user designed custom hardware accelerators!
  Template HDL file provided, compiles with already placed and routed static logic

## Slide 20
FPGA
VFR
VFR
Input Arbiter
Soft
Processor
Output Queues
Bus
Stream Interface
Agent (Host PC)
JTAG
DRAM
MACs
FPGA System-Level Architecture

## Slide 21: Packet Forwarding and Interface Policing
Input arbiter uses a CAM to match incoming packet dst field to correct VFR – no match? Drop
  CAM programmable by soft proc, which receives MAC from agent
Input Arbiter
CAM
to VFR_0
to VFR_n
. . .
MACs
Bus
Pkt In Stream

## Slide 22
FPGA
VFR
VFR
Input Arbiter
Soft
Processor
Output Queues
Bus
Stream Interface
Agent (Host PC)
JTAG
DRAM
MACs
FPGA System-Level Architecture

## Slide 23
VFR – User Logic
MMap Register
PR Interface Enable
PR Reset
Stream Out
Stream In
System Partial Reconfiguration Control
Mem Op Queues
(Bus Master)
Bus to Soft Proc, DRAM
Streams frozen after current transaction finishes – no fragmented pkts!

## Slide 24: What else can we use this for?
Line rate packet processing
  Custom firewalls
  Rate limiters
  Custom traffic classifiers
Any other type of accelerator
  With data sent over Ethernet

## Slide 25: SAVI
Smart Applications on Virtual Infrastructure
  Canada-wide experimental research network
SAVI Testbed
  OpenStack based cloud computing infrastructure
  Linux KVM based Virtual Machines
  Complete tenant isolation
  GPUs + Reconfigurable Hardware
  OpenFlow SDN + network virtualization

## Slide 26
Server
Hypervisor
Agent
VM
VM
. . .
FPGA(s)
VFR
VFR
. . .
Server
Agent
OpenStack Controller
Resource DB
API
OpenFlow Network

## Slide 27: Software Defined Networking, OpenFlow
Separation of control plane and forwarding hardware
Control Plane (Software)
OpenFlow Protocol
Image Credit: Nick McKeown

## Slide 28
28
Network OS
App
App
OpenFlow Protocol
API
Image Credit: Nick McKeown
Network 1
Network 2

## Slide 29: Switches
Switches are now dumb forwarding logic
  Rule tables are set by the controller software
  Basic operation: pkt in, match, action
Now we have a complete view of the entire network
  Which enables complete control

## Slide 30: Accelerator Chaining
OpenFlow controls the flow of packets/data
  Accelerators process normally, do not worry about forwarding
Down
Sample
Transcode
Encrypt
OpenFlow Network

## Slide 31: Accelerator Chaining
Simpler hardware
  Need not worry about forwarding
  Complex forwarding control moved to software
Partitioned designs
  Spread across multiple VFRs
  Enabling large and complex processing pipelines
  Maintaining high throughput
  Easier debugging?
Downside – must design your own OpenFlow controller

## Slide 32: Performance
Still under investigation
Boot latency
  From command entry to point that accelerator can process packets
    Approximately 2.6 seconds – much faster than a VM!
Overhead cost of virtualization (static logic)?
  Simulations show 3 cycles latency difference from non-virtualized system

## Slide 33: To Wrap Up
Virtualized FPGA resources in the cloud
  Same boot command as a virtual machine
Dynamically scalable and flexible hardware acceleration
User designed, user controlled
Prototype implemented, work is ongoing

## Slide 34: Thanks! Questions?

## Slide 35: Research Applications with SAVI
SAVI Testbed is based on OpenStack
  Our prototype is implemented within the SAVI Testbed
SAVI has virtualized networks
  We can get our own isolated custom-controlled Ethernet network
  Can enable testing of non-IP Internet-routing protocols
  VFRs could provide line rate routing infrastructure for these non-IP networks
    Facilitate wide area, large scale testing of future protocols in true Layer 3 – i.e. not on top of IP

## Slide 36
1 Region:
~12,000 Slices
Virtex 5 VTX240T