## Slide 1: The Case for Embedding Networks-on-Chip in FPGA Architectures
Vaughn Betz
University of Toronto
With special thanks to Mohamed Abdelfattah, Andrew Bitar and Kevin Murray

## Slide 2: Overview
Why do we need a new system-level interconnect?
Why an embedded NoC?
How does it work?
How efficient is it?
Future trends and an embedded NoC
  Data center FPGAs
  Silicon interposers
  Registered routing
  Kernels  massively parallel accelerators

## Slide 3: Why Do We Need a System Level Interconnect?
And Why a NoC?

## Slide 4
Module 1
Module 2
Module 3
Module 4
Challenge
Large Systems
High bandwidth hard blocks & compute modules
High on-chip communication
PCIe
PCIe

## Slide 5
Bus 1
Bus 2
Bus 3
Module 4
Module 1
Module 3
Module 2
Today
Wide links from single bit-programmable interconnect
Somewhat unpredictable frequency  re-pipeline
100s of bits
Tough timing constraints
Physical distance affects frequency
Buses are unique to the application  design time
Design soft bus per set of connections
Muxing/arbitration/buffers on wide datapaths  big
System-level buses  costly
PCIe
PCIe
100’s of muxes
Notes: Wide links:
  FPGAs are good at doing things in parallel which compensates for their relatively low operating frequency
  Wide functional units = wide connections to be able to transport the high bandwidth data
  Only gets worse – need more data, more bandwidth, more issues
  Harder to design the buses
  Worse timing closure
Timing:
  Physical distance affects timing: the farther you are, the more switches and wire segments you are using.
  As a designer I can only know that timing information after placement and routing
    Takes a long time
    Must then go back and redesign the interconnect to meet constraints
    Time/effort consuming!
Area:
  Will show you some results that highlight how big buses are
  Multiple clock domains require area-expensive asynchronous fifos
Why?
Do we really need all that flexibility in the system-level interconnect? No
Is there a better way?  this is the question that my research attempts to answer
We think an embedded NoC is the way to go

## Slide 6
Hard Bus?
System-level interconnect in most designs?
Costly in area & power?


Module 4
Module 1
Module 3
Module 2
dedicated (hard) wires
Muxing, arbitration
Bus 1
Bus 2
Bus 3
Bus 1
Bus 2
Bus 3
Module 4
Module 1
Module 3
Module 2
PCIe
PCIe
Usable by many designs?
Notes: Wide links:
  FPGAs are good at doing things in parallel which compensates for their relatively low operating frequency
  Wide functional units = wide connections to be able to transport the high bandwidth data
  Only gets worse – need more data, more bandwidth, more issues
  Harder to design the buses
  Worse timing closure
Timing:
  Physical distance affects timing: the farther you are, the more switches and wire segments you are using.
  As a designer I can only know that timing information after placement and routing
    Takes a long time
    Must then go back and redesign the interconnect to meet constraints
    Time/effort consuming!
Area:
  Will show you some results that highlight how big buses are
  Multiple clock domains require area-expensive asynchronous fifos
Why?
Do we really need all that flexibility in the system-level interconnect? No
Is there a better way?  this is the question that my research attempts to answer
We think an embedded NoC is the way to go

## Slide 7
PCIe
PCIe
Hard Bus?
System-level interconnect in most designs?
Costly in area & power?


Module 4
Module 1
Module 3
Module 2
Bus 1
Bus 2
Bus 3
Usable by many designs?
Module 4
Module 1
Module 3
Module 2
Module 5
Not Reusable!
Too design specific

Notes: Wide links:
  FPGAs are good at doing things in parallel which compensates for their relatively low operating frequency
  Wide functional units = wide connections to be able to transport the high bandwidth data
  Only gets worse – need more data, more bandwidth, more issues
  Harder to design the buses
  Worse timing closure
Timing:
  Physical distance affects timing: the farther you are, the more switches and wire segments you are using.
  As a designer I can only know that timing information after placement and routing
    Takes a long time
    Must then go back and redesign the interconnect to meet constraints
    Time/effort consuming!
Area:
  Will show you some results that highlight how big buses are
  Multiple clock domains require area-expensive asynchronous fifos
Why?
Do we really need all that flexibility in the system-level interconnect? No
Is there a better way?  this is the question that my research attempts to answer
We think an embedded NoC is the way to go

## Slide 8: Needed: A More General System-Level Interconnect
Move data between arbitrary end-points
Area efficient
High bandwidth  match on-chip & I/O bandwidths
Network-on-Chip (NoC)

## Slide 9
Embedded NoC
Module 4
Module 1
Module 3
Module 2
Data
Packet
flit
flit
flit
Data
NoC=complete interconnect
  Data transport
  Switching
  Buffering
Links
Routers
PCIe
PCIe
Notes: We think the right answer is an embedded NoC
When fpga vendors realised that some functions were common enough they hardened them
Hardened DSP blocks are much more efficient than soft dsps
Blockram was much needed to build efficient memories
Same is true for IO transceivers and memory controllers
I believe we could make a similar case for interconnect:
Applications on fpgas are large and modular – inter-module communication (or sys-level communication) is significant in almost every design.
Take DDR memory for example: every sizable fpga application accesses off-chip memory – that immediately means wide buses with tough timing constraints and multiple clock domains.
For this precise piece of an application – access to ddr – our work shows that an embedded NoC can be quite a bit more efficient. (show micro results)
Someone could be wondering why harden an NoC, why not a bus: When we thought of hardening a bus, we couldn’t figure out where the endpoints should be – wherever they are placed it won’t be flexible enough
whereas NoCs on the other hand are the most distributed type of on-chip interconnect.
NoCs are a type of interconnect that are commonly used to connect cores in a multi-core or multiprocessor chip
We do not intend, nor are we trying to reinvent the wheel – we want to use the very same NoCs used in the multiprocessor field.
To transport data, we add some control information to form a packet (terminology we’ll be using)
That packet is then split up into flits.
Flits are transmitted to the specified destination.
The main thing here is that we want to adapt this NoC to work with conventional FPGA design – we aren’t trying to change how FPGA designers do their work. We’re just trying to make it easier for them.

## Slide 10
Embedded NoC
Module 4
Module 1
Module 3
Module 2
Module 5
PCIe
PCIe
Data
Packet
flit
flit
flit
Data
NoC=complete interconnect
  Data transport
  Switching
  Buffering
Moves data between arbitrary end points?

Notes: We think the right answer is an embedded NoC
When fpga vendors realised that some functions were common enough they hardened them
Hardened DSP blocks are much more efficient than soft dsps
Blockram was much needed to build efficient memories
Same is true for IO transceivers and memory controllers
I believe we could make a similar case for interconnect:
Applications on fpgas are large and modular – inter-module communication (or sys-level communication) is significant in almost every design.
Take DDR memory for example: every sizable fpga application accesses off-chip memory – that immediately means wide buses with tough timing constraints and multiple clock domains.
For this precise piece of an application – access to ddr – our work shows that an embedded NoC can be quite a bit more efficient. (show micro results)
Someone could be wondering why harden an NoC, why not a bus: When we thought of hardening a bus, we couldn’t figure out where the endpoints should be – wherever they are placed it won’t be flexible enough
whereas NoCs on the other hand are the most distributed type of on-chip interconnect.
NoCs are a type of interconnect that are commonly used to connect cores in a multi-core or multiprocessor chip
We do not intend, nor are we trying to reinvent the wheel – we want to use the very same NoCs used in the multiprocessor field.
To transport data, we add some control information to form a packet (terminology we’ll be using)
That packet is then split up into flits.
Flits are transmitted to the specified destination.
The main thing here is that we want to adapt this NoC to work with conventional FPGA design – we aren’t trying to change how FPGA designers do their work. We’re just trying to make it easier for them.

## Slide 11: Embedded NoC Architecture
How Do We Build It?

## Slide 12: Routers, Links and Fabric Ports
No hard boundaries
   Build any size compute modules in fabric
Fabric interface: flexible interface to compute modules

## Slide 13: Router
Full featured virtual channel router [D. Becker, Stanford PhD, 2012]

## Slide 14: Must We Harden the Router?
Tested: 32-bit wide ports, 2 VCs, 10 flit deep buffers
65 nm TSMC process standard cells vs. 65 nm Stratix III
Y | Soft | Hard
Area | 4.1 mm2 (1X) | 0.14 mm2 (30X)
Speed | 166 MHz (1X) | 943 MHz (5.7X)
Hard: 170X throughput per area!

## Slide 15: Harden the Routers?
FPGA-optimized soft router?
  [CONNECT, Papamichale & Hoe, FPGA 2012] and [Split/Merge, Huan & Dehon, FPT 2012]
    ~2-3X throughput / area improvement with reduced feature set
  [Hoplite, Kapre & Gray, FPL 2015]
    Larger improvement with very reduced features / guarantees
Not enough to close 170X gap with hard
Want ease of use  full featured
Hard Routers

## Slide 16: Fabric Interface
200 MHz module, 900 MHz router?
Configurable time-domain mux / demux: match bandwidth
Asynchronous FIFO: cross clock domains
 Full NoC bandwidth, w/o clock restrictions on modules

## Slide 17: Hard Routers/Soft Links
FPGA
Router
Same I/O mux structure as a logic block – 9X the area
Conventional FPGA interconnect between routers
Logic clusters

## Slide 18: Hard Routers/Soft Links
FPGA
Router
Same I/O mux structure as a logic block – 9X the area
Conventional FPGA interconnect between routers
730 MHz
Faster, fewer wires (C12)

## Slide 19: Hard Routers/Soft Links
Router
Assumed a mesh  Can form any topology
FPGA

## Slide 20: Hard Routers/Hard Links
FPGA
Router
Muxes on router-fabric interface only – 7X logic block area
Dedicated interconnect between routers  Faster/Fixed
Logic blocks

## Slide 21: Hard Routers/Hard Links
FPGA
Router
Muxes on router-fabric interface only – 7X logic block area
Dedicated interconnect between routers  Faster/Fixed
900 MHz
Dedicated Interconnect (Hard Links)
~ 9 mm at 1.1 V or ~ 7 mm at 0.9V

## Slide 22: Hard NoCs
 | Soft | Hard (+ Soft Links) | Hard (+ Hard Links)
Area | 4.1 mm2 (1X) | 0.18 mm2 = 9 LABs (22X) | 0.15 mm2 =7 LABs (27X)
Speed | 166 MHz (1X) | 730 MHz (4.4X) | 943 MHz (5.7X)
Power | -- | (9X less) | (11X – 15X)
Router

## Slide 23: Hard NoCs
Router
 | Soft | Hard (+ Soft Links) | Hard (+ Hard Links)
Area | 4.1 mm2 (1X) | 0.18 mm2 = 9 LABs (22X) | 0.15 mm2 =7 LABs (27X)
Speed | 166 MHz (1X) | 730 MHz (4.4X) | 943 MHz (5.7X)
Power | -- | (9X less) | (11X – 15X less)

## Slide 24: 2. Area Efficient?
64-node, 32-bit wide NoC on Stratix V
Very Cheap! Less than cost of 3 soft nodes
 | Soft | Hard (+ Soft Links) | Hard (+ Hard Links)
Area | ~12,500 LABs | 576 LABs | 448 LABs
%LABs | 33 % | 1.6 % | 1.3%
%FPGA | 12 % | 0.6 % | 0.45%


## Slide 25: Power Efficient?
Hard and Mixed NoCs  Power Efficient
Length of 1 NoC Link
200 MHz
Compare to best case FPGA interconnect: point-to-point link
64 Width, 0.9 V, 1 VC

## Slide 26: 3. Match I/O Bandwidths?
32-bit wide NoC @ 28 nm
1.2 GHz  4.8 GB/s per link
Too low for easy I/O use!

## Slide 27: 3. Match I/O Bandwidths?
Need higher-bandwidth links
  150 bits wide @ 1.2 GHz
  22.5 GB/s per link
  Can carry full I/O bandwidth on one link
Want to keep cost low
  Much easier to justify adding to an FPGA if cheap
    E.g. Stratix I: 2% of die size for DSP blocks
    First generation: not used by most customers, but 2% cost OK
  Reduce number of nodes: 64  16
    1.3% of core area for a large Stratix V FPGA


## Slide 28: NoC Usage & Application Efficiency Studies
How Do We Use It?

## Slide 29: FabricPort In
Ready/Valid
Any* width
0-600 bits
Frequency
1.2 GHz
Credits
Fixed Width
150 bits
Frequency
100-400 MHz
FPGA Module
Embedded NoC
Width
# flits
0-150 bits
1
150-300 bits
2
300-450 bits
3
450-600 bits
4

## Slide 30: FabricPort In
3
Ready/Valid
Any* width
0-600 bits
Frequency
1.2 GHz
Credits
Fixed Width
150 bits
Frequency
100-400 MHz
FPGA Module
Embedded NoC
Time-domain multiplexing:
Divide width by 4
Multiply frequency by 4

## Slide 31: FabricPort In
3
Ready/Valid
Any* width
0-600 bits
Frequency
1.2 GHz
Credits
Fixed Width
150 bits
Frequency
100-400 MHz
FPGA Module
Embedded NoC
Asynchronous FIFO:
Cross into NoC clock
No restriction on module frequency
Time-domain multiplexing:
Divide width by 4
Multiply frequency by 4

## Slide 32: FabricPort In
3
Ready/Valid
Any* width
0-600 bits
Frequency
1.2 GHz
Credits
Fixed Width
150 bits
Frequency
100-400 MHz
FPGA Module
Embedded NoC
Asynchronous FIFO:
Cross into NoC clock
No restriction on module frequency
Time-domain multiplexing:
Divide width by 4
Multiply frequency by 4
NoC Writer:
Track available buffers in NoC Router
Forward flits to NoC
Backpressure
2
1
0
Ready=0
Input interface: flexible & easy for designers  little soft logic

## Slide 33: Designer Use
NoC has non-zero, usually variable latency
Use on latency-insensitive channels
Stallable modules
A
B
C
data
data
valid
ready
Permapaths
A
B
C
A
With restrictions, usable for fixed-latency communication
  Pre-establish and reserve paths
  “Permapaths”

## Slide 34: How Common Are Latency-Insensitive Channels?
Connections to I/O
  DDRx, PCIe, …
  Variable latency
Between HLS kernels
  OpenCL channels / pipes
  Bluespec SV
  …
Common design style between larger modules
  And any module can be converted to use [Carloni et al, TCAD, 2001]
Widely used at system level, and use likely to increase

## Slide 35: Packet Ordering
FPGA Designs
Mostly streaming
Cannot tolerate reordering
  Hardware expensive and difficult
Multiprocessors
Memory mapped
Packets arrive out-of-order
  Fine for cache lines
  Processors have re-order buffers
1
2
All packets with same src/dst must take same NoC path
RULE
FULL
2
1
1
2
All packets with same src/dst must take same VC
RULE

## Slide 36: Application Efficiency Studies
How Efficient Is It?

## Slide 37: 1. Qsys vs. NoC
qsys: build logical bus from fabric
NoC: 16-nodes, hard routers & links

## Slide 38: Area Comparison
Only 1/8 of Hard NoC BW used, but already less area for most systems

## Slide 39: Power Comparison
Hard NoC saves power for even simplest systems

## Slide 40: 2. Ethernet Switch
FPGAs with transceivers: commonly manipulating / switching packets
e.g. 16x16 Ethernet switch, @ 10 Gb/s per channel
Transceiver
NoC
Router
NoC is the crossbar
Plus buffering, distributed arbitration & back-pressure
Fabric inspects packet headers, performs more buffering, …

## Slide 41: Ethernet Switch Efficiency
14X more efficient!
Latest FPGAs: ~2 Tb/s transceiver bandwidth  need good switches

## Slide 42: 3. Parallel JPEG (Latency Sensitive)
NoC makes performance more predictable
NoC doesn’t produce wiring hotspots & saves long wires
Max 40%
Max 100%
[long wires]

## Slide 43: Future Trends and Embedded NoCs
Speculation Ahead!

## Slide 44: 1. Embedded NoCs and the Datacenter

## Slide 45: Datacenter Accelerators
Microsoft Catapult: Shell & Role to Ease Design
Shell: 23% of Stratix V FPGA [Putnam et al, ISCA 2014]

## Slide 46: Datacenter “Shell”: Bus Overhead
Buses to I/Os in shell & role
Divided into two parts to ease compilation (shell portion locked down)

## Slide 47: Datacenter “Shell”: Swapping Accelerators
Partial reconfig of role only  swap accelerator w/o taking down system
Overengineer shell buses for most demanding accelerator
Two separate compiles  lose some optimization of bus

## Slide 48: More Swappable Accelerators
Allows more virtualization
But shell complexity increases
Less efficient
Wasteful for one big accelerator
Accelerator 5
Accelerator 6
Big Accelerator

## Slide 49: Shell with an Embedded NoC
Efficient for more cases (small or big accelerators)
Data brought into accelerator, not just to edge with locked bus
Accelerator 6
Accelerator 5
Big Accelerator

## Slide 50: 2. Interposer-Based FPGAs

## Slide 51: Xilinx: Larger Fabric with Interposers
Create a larger FPGA with interposers
10,000 connections between dice (23% of normal routing)
Routability good if > 20% of normal wiring cross interposer [Nasiri et al, TVLSI, to appear]
Figure: Xilinx, SSI Technology White Paper, 2012

## Slide 52: Interposer Scaling
Figure: Xilinx, SSI Technology White Paper, 2012
Concerns about how well microbumps will scale
Will interposer routing bandwidth remain >20% of within-die bandwidth?
Embedded NoC: naturally multiplies routing bandwidth (higher clock rate on NoC wires crossing interposer)

## Slide 53: Altera: Heterogeneous Interposers
Custom wiring interface to each unique die
  PCIe/transceiver, high-bandwidth memory
NoC: standardize interface, allow TDM-ing of wires
Extends system level interconnect beyond one die
Figure: Mike Hutton, Altera Stratix 10, FPL 2015

## Slide 54: 3. Registered Routing

## Slide 55: Registered Routing
Stratix 10 includes a pulse latch in each routing driver
  Enables deeper interconnect pipelining
  Obviates need for a new system-level interconnect?
I don’t think so
  Makes it easier to run wires faster
  But still not:
    Switching, buffering, arbitration (complete interconnect)
    Pre-timing closed
    Abstraction to compose & re-configure systems
Pushes more designers to latency-tolerant techniques
  Which helps match the main NoC programming model

## Slide 56: 4. Kernels  Massively Parallel Accelerators
Crossbars for Design Composition

## Slide 57: Map – Reduce and FPGAs
[Ghasemi & Chow, MASc thesis, 2015]
Write map & reduce kernel
Use Spark infrastructure to distribute data & kernels across many CPUs
Do same for FPGAs?
Between chips  network
Within a chip  soft logic
Consumes lots of soft logic and limits routable design to ~30% utilization!

## Slide 58: Can We Remove the Crossbar?
Not without breaking Map-Reduce/Spark abstraction!
  The automatic partitioning / routing / merging of data is what makes Spark easy to program
  Need a crossbar to match the abstraction and make composability easy
NoC: efficient, distributed crossbar
  Allows us to efficiently compose kernels
  Can use crossbar abstraction within chips (NoC) and between chips (datacenter network)

## Slide 59: Wrap Up

## Slide 60: Wrap Up
Adding NoCs to FPGAs
  Enhances efficiency of system level interconnect
  Enables new abstractions (crossbar composability, easily-swappable accelerators)
NoC abstraction can cross interposer boundaries
  Interesting multi-die systems
My belief:
  Special purpose box  datacenter
  ASIC-like flow  composable flow
  Embedded NoCs help make this happen

## Slide 61: Future Work
CAD System for Embedded NoCs
  Automatically create lightweight soft logic to connect to fabric port (translator)
    According to designer’s specified intent
  Choose best router to connect each compute module
  Choose when to use NoC vs. soft links
Then map more applications, using CAD