## Slide 1: Spatial Architectures in the More-than-Moore and Deep Learning Era Vaughn Betz University of Toronto & Cerebras Systems with thanks to Andrew Boutros, Sean Lie and all my students for some slide content

## Slide 2: DL Inference: Energy Efficiency and Latency Matter
Nvidia Drive AGX Pegasus (2022)
Up to 750W
Low inference latency crucial for safety!
~9% of US electricity demand by 2030 [1]
Low inference latency enables reasoning and cascade of AI algorithms/agents!
Key metric is
Perf / W / $
Power is ~30% of cost
[1] R. Leppert, “What we know about energy US at U.S. data centers amid the AI boom,” Pew Research Center, Oct. 24, 2205.
Chevy Bolt
~6 kW in city

## Slide 3: FPGA Strength: Specialize, Shrink Operands
Can reprogram FPGA to implement exact hardware needed by network
  Perform only necessary operation, w/o instruction stream
  Programmable routing: directly wire data from one unit to another
  Programmable logic: use minimum operand size/type needed for accuracy
A. Boutros, A. Arora and V. Betz, “Field-Programmable Gate Array Architecture for Deep Learning: Survey & Future Directions,” Proceedings of the IEEE, 2025,

## Slide 4: Spatial Compute Strength  Data Locality
Need to keep data close to compute
Leaving chip very expensive!
128 byte op
128 byte reads
On chip (3 nm)
Interposer
PCB
Interposer

## Slide 5: Spatial Compute Strength  Data Locality
Huge flexibility in combining RAMs with programmable logic & routing
~Pb/s of on-chip bandwidth
Split into 10,000+ independent blocks
Can create right size of RAM
Can locate near operators
Integrate with logic, e.g. custom scatter/gather to exploit sparsity
Challenge: largest networks  off-chip memory → weakens advantage
Narrow & Deep
Wide & Shallow
XBAR
Independent
RAM Blocks
Logic Blocks
DSP Blocks

## Slide 6: FPGA Strength: Low Latency, Highly Flexible I/O
Programmable I/O (DDR, …)
Programmable Serial I/O (PCIe,...)
6
Embedded: low latency & custom I/O
Custom I/O
Preprocess & Feature Extract
DL
FPGA

## Slide 7: FPGA Weakness: Programmability Overhead
Programmability is expensive!
LEs and programmable routing larger & slower than gates & wires
Can we make soft fabrics more efficient for DL?
Harden key functions?
Connect with programmable routing, dedicated interconnect, or NoC?
DSP Block

## Slide 8: Example Accelerator Styles To Maximize FPGA Advantages

## Slide 9: Dataflow: HPIPE
Efficient CNN Inference

## Slide 10: HPIPE Design Philosophy
M. Hall et al, “From TensorFlow Graphs to LUTs and Wires: Automated Sparse and Physically Aware CNN Hardware Generation“, FPT 2020
Conv2D 7x7, stride 2
Conv2D 5x5, stride 1
Conv2D 3x3, stride 1
PE
PE
PE
Buffer
Map
Map
Map
Commonly → Temporal mapping on PE arrays
Sequential processing of layers
PEs handle any layer → lower efficiency
Conv2D 7x7, stride 2
Conv2D 5x5, stride 1
Conv2D 3x3, stride 1
PE
PE
PE
Map
Map
Map
Instead → Spatial mapping to specialized units
Per-layer custom HW → higher efficiency
Latency-insensitive interfaces between layers
Exploit pipeline parallelism

## Slide 11: Specialized Hardware and Local Data Movement
Maximum specialization
No instruction decode overhead
Spatial layout  data is local
Needs different hardware for every network
Build a domain-specific compiler

## Slide 12: Auto Generation of Custom CNN HW (HPIPE)
Fuse layers for more efficient implementations
HW Specifications
TensorFlow Model Description
Graph Optimization
Resource Allocation
RTL Generation
FPGA Bitstream
HPIPE
A pipeline is as slow as its slowest stage
Balance layer throughput to increase efficiency
Generate specialized HW for each layer from highly optimized templates
M. Hall et al, “From TensorFlow Graphs to LUTs and Wires: Automated Sparse and Physically Aware CNN Hardware Generation“, FPT 2020
Placement-Aware Pipelining and Memory Mapping
Spatial-aware memory structures, deep pipelining and locality-optimized communication

## Slide 13: Results vs. GPU s(AI-Optimized Stratix 10 FPGA)
17x higher batch-1 throughput vs. V100 GPU at lower latency
1.3x higher batch-128 throughput vs. V100 GPU at 3x lower latency
Strength: latency, efficiency
Weakness: large models may not fit in on-chip memory
M. Stan et al, “HPIPE NX: Boosting CNN Inference Acceleration Performance with AI-Optimized FPGAs“, FPT, 2022.

## Slide 14
More memory  fit parameters of large CNNs
More compute resources  higher throughput & lower latency
Moderate data between chips  easily fits on 100 Gb ethernet
Devices needed scales with model size  exceeds budget & compute needs of some embedded applications
Conv2D
MaxPool
ReLU
Conv2D
Conv2D
BiasAdd
Add
100 Gb
Ethernet
FPGA1
FPGA2
Supporting Very Large CNNs: Multi-FPGA Pipeline
MobileNet-V1
MobileNet-V2
85% sparse ResNet-50
top-1: 72%
top-1: 72%
top-1: 72%
top-1: 72%
top-1: 72%
top-1: 72%
Near linear scaling in latency & throughput with device count
M. Doumet et al, “H2PIPE: High Throughput CNN Interfence on FPGAs with High Bandwidth Memory,” FPL, 2024

## Slide 15: Supporting Very Large CNNs: Selective Weight Offload
Venieris et al.
Liu et al.
5.1x
H2PIPE
FTDL
DNNVM
Offload weights that free up maximum on-chip memory with minimum performance loss
Lose some performance, but larger networks fit on one FPGA
Still higher throughput than prior work
Cost / performance trade-off vs. multi-FPGA pipeline
M. Ibrahim et al, “Extending Data Flow Architectures for Convolutional Neural Networks to Multiple FPGAs,” FPT, 2023
HBM

## Slide 16: Overlay: NPU
Software Programmable Inference

## Slide 17: Overlay Design Flow
Implement in RTL
Applications
FPGA CAD Tools
Bitstreams
Perf?
Y
N
Domain Requirements
Design HW/SW Contract (ISA)
Develop SW Toolchain
Develop overlay via traditional flow
Applications
Implement in SW
Overlay Compiler
Binaries
Bitstream
Traditional Flow
Overlay Flow
HW Experts
Data Scientist
App Expert
Long compiles, Application experts designing HW
Fast compiles, Application experts write (custom) software

## Slide 18: Neural Processing Unit (NPU)
Targets MLPs, RNNs, GRUs, LSTMs, GNNs
Very Long Instruction Word (VLIW) soft processor - 5 coarse grained stages
Amortize control → Single instruction executes 45,000 operations
Customize memory subsystem  Exploit tremendous on-chip memory BW
Data cascades from one stage to next  spatial locality
A. Boutros et al, “Beyond Peak Performance: Comparing the Real Performance of AI-Optimized FPGAs and GPUs“, FPT, 2020

## Slide 19: Results vs. Same-Generation DL-Optimized GPUs
A. Boutros et al, “Beyond Peak Performance: Comparing the Real Performance of AI-Optimized FPGAs and GPUs“, FPT, 2020
11x vs. V100
23x vs. T4
AI-Optimized FPGA with Tensor Blocks
High performance, yet software programmable

## Slide 20: Application Case Study: 5G MIMO Scheduling
5G Networks: schedule freq. bands and antennas, with very low latency
GCN layer
GCN layer
GAT layer
Sum + Update
Model as 3 coupled GNNs
< 80 s for 100 users!
Leverages FPGA strengths: low-latency, complete system, custom I/O
T. Zhang et al, “A Software-Programmable Neural Processing Unit for Graph Neural Network Inference on FPGAs,” FPL, 2024

## Slide 21: Finding Better FPGA Architectures for Deep Learning
Ideas, Tools and Flows

## Slide 22: Logic Structures that Favour Arithmetic
M. Eldafrawy et al, “FPGA Logic Block Architectures for Efficient Deep Learning Inference,” TRETS, 2020
J. Pun et al, “Double Duty: FPGA Architecture to Enable Concurrent LUT and Adder Chain Usage”, FPL 2025
4-bits of arithmetic per 6-LUT
50% density increase for soft MACs
<3% tile size increase
Independent use of 5-LUTs & adders
25% density increase unrolled DNNs
< 4% tile size increase

## Slide 23: Harden Key Computations?
A. Boutros and V. Betz, “FPGA Architecture: Principles and Progression,” IEEE Circuits and Systems Magazine, May 2021
Programmable logic vs. ASIC gates:
~30x area, ~3x speed [Kuon & Rose, TCAD, 2007]
Gains lower once internal programmability and connectivity to routing added
E.g. DSP blocks fully used for FIR filters: 8.5x area, 2.5x speed
DSP Block
Must consider routing & range of uses in hardening choice

## Slide 24: Example: Intel Stratix 10 NX Tensor Block
30x int8 multipliers instead of 2x int18 multipliers
Or 60x int4 multipliers
30x int8
Focusing on this mode
Multiplier area  precision2  can fit many 8x8 within DSP footprint
Notes: The int8 tensor mode implements 30 int8 multipliers in a single block, instead of 2 int18 multipliers.

## Slide 25: Tensor Block int8
30x int8 multipliers instead of 2x int18 multipliers
480 inputs
480 outputs
DSP block: 96 inputs
DSP block: 72 outputs
Notes: But, if you think about it, 30 int8 multipliers would require 480 input and output ports which would be significantly more expensive in terms of area.

## Slide 26
480 inputs
72 outputs
30x int8 multipliers instead of 2x int18 multipliers
Limit Outputs: Arrange multipliers as 3x dot-10 engines + accumulators
Dedicated Cascades: Cheap
Tensor Block int8
Notes: To drive down the number of output ports, the 30 multipliers are arranged as three 10 element dot products with internal reduction and optional 24-bit accumulators which brings down the number of output ports to only 72 ports.

## Slide 27
30x int8 multipliers instead of 2x int18 multipliers
Limit Outputs: Arrange multipliers as 3x dot-10 engines + accumulators
Limit Inputs: Broadcast one set of inputs to all dot-10 engines
320 inputs
72 outputs
Tensor Block int8
Notes: Then to solve the inputs problem, one set of input is shared by broadcasting it to all 3 dot-10 engines …

## Slide 28
30x int8 multipliers instead of 2x int18 multipliers
Limit Outputs: Arrange multipliers as 3x dot-10 engines + accumulators
Limit Inputs: Broadcast one set of inputs to all dot-10 engines
Limit Inputs: Ping-pong input reuse chain loaded from the block above
80 inputs
72 outputs
Tensor Block int8
Notes: And the other set of input is loaded from the tensor block above using a dedicated input reuse chain in which one set of registers can be loaded while the other is used for compute in a ping-pong fashion.
This brings the total number of needed input ports to only 80.

## Slide 29
30x int8 multipliers instead of 2x int18 multipliers
Limit Outputs: Arrange multipliers as 3x dot-10 engines + accumulators
Limit Inputs: Broadcast one set of inputs to all dot-10 engines
Limit Inputs: Ping-pong input reuse chain loaded from the block above
80 inputs
72 outputs
15x peak int8 TOPS in similar area to DSP block
with a more constrained dot-product with re-use unit
Tensor Block int8
Notes: And the other set of input is loaded from the tensor block above using a dedicated input reuse chain in which one set of registers can be loaded while the other is used for compute in a ping-pong fashion.
This brings the total number of needed input ports to only 80.

## Slide 30: Tools to Explore the Next Generation of FPGAs
Verilog-to-Routing

## Slide 31: FPGA Architecture Research Flow
Challenges:
Need representative application designs
Describe FPGA Architecture & Low Level Circuit Area, Power, Delay
Need retargettable CAD flow
Designs
FPGA Architecture #1
Speed/Area/
Power
FPGA Architecture #2
Speed/Area/
Power
Need CAD Flow for Architecture #1
Need CAD Flow for Architecture #2

## Slide 32: Verilog to Routing (VTR) Overall Flow
Pack
Place
Route
Analysis
STA
Netlist
Verilog Designs
VPR
Architecture
QoR / Reports
Open Source FPGA CAD Flow
Connect to Yosys, Odin-II or combination for synthesis
VPR for placement, routing, analysis
Approach:
Architecture Agnostic
Data-driven FPGA Architecture description
ODIN II
ABC
ABC
Fasm, fpga-bitstream, other bitstream gen.
Parmys
Yosys
M. Elgammal et al, “VTR 9: Open-Source CAD for Fabric and Beyond FPGA Architecture Exploration", TRETS, 2025.

## Slide 33: Architecture Flexibility: Blocks
4-LUT
6-LUT
?
Logic Primitive
Logic Block Size
Inter-Element Connectivity
Logic Element
+
Full Blocks
DSP Block

## Slide 34: Architecture Flexibility: Block Arrangement
Block RAM
IOs
DSP
Hard
Block
NoC
Router
Logic Block

## Slide 35: Architecture Flexibility: Routing
Block Input Connection
Block Output Connection
Wire-Wire Connections
(switch-block)
Routing
Wires
Direct Block-Block Connection

## Slide 36: Hardened Networks on Chip
Packet-switched router
NoC Link
NoC for system-level communication (e.g. with DDR, HBM, PCIe)
Placement co-optimizes NoC and programmable routing usage
NoC-connected accelerators (e.g. matrix-matrix systolic array)?
S. Srinivasan et al, “Placement Optimization for NoC-Enhanced FPGAs“, FCCM, 2023

## Slide 37: 3D (Stacked Die) FPGAs
A. Boutros et al, “Into the Third Dimension: Architecture Exploration Tools for 3D Reconfigurable Acceleration Devices,” FPT, 2023
Feasible with hybrid bonding
Feasible with bumps
Larger capacity FPGAs
More local communication
Integrate different technologies
Bring larger memory very close to compute
Separate out design of specific accelerator
3D Systems + Spatial Arch.: High Locality, Near Memory Compute

## Slide 38: Beyond Exploration: Custom FPGA Implementation
X. Tang et al, "OpenFPGA: An Open-Source Framework for Agile Prototyping Customizable FPGAs," IEEE Micro, 2020
I. Youssef, “LaZagna: An Open-Source Framework for 3D FPGA Architectural Exploration,” ICCAD, 2025
OpenFPGA (QuickLogic, RapidSilicon, RapidFlex)
ZeroASIC Platypus
Can now go from VTR arch file  standard cell layout automatically
Cost: ~60% more area and ~20% more delay for soft fabric than full custom
Massively reduces the NRE to create a unique FPGA system
    Blocks specialized for specific DL ops (e.g. fp4 matrix-vector)?
    NoCs connecting to systolic matrix-matrix multipliers?
    Mix FPGA/spatial logic for some operations with temporal (processor) logic for others?

## Slide 39: Wafer-Scale Integration and the Cerebras Spatial-Temporal Architecture

## Slide 40: Why Wafer Scale?
Scale up to a very large parallel system, without bottlenecks and energy of multi-chip interconnect
Keep your friends close and your data closer!
Blackwell GB300 GPU
8x HBM3e Interposer
192 GB
0.008 PB/s
WSE-3 Local SRAM Distributed on-wafer
44 GB
21 PB/s
NVIDIA GB300: two reticle limit (~850 mm2) dice + 8 HBM stacks, all on silicon interposer
Cerebras WSE-3: 46,000 mm2 wafer-scale

## Slide 41: WSE-3 vs. Nvidia H100 Scale Comparison
S. Li, “Wafer-Scale AI: GPU Impossible Performance,” Hot Chips, 2024.

## Slide 42: Temporal and Spatial Compute
Temporal: Computation Variability Over Time
FPGAs
Spatial: Distribution of Data
Hierarchical, Implicit
Spatial,
Explicit
High
Low
CPUs
CGRAs
GPUs
AMD AIEs
Cerebras WSE
High temporal flexibility
Minimal control overhead
Spatio-Temporal architectures

## Slide 43: Throughput-Focused Spatio-Temporal Arch
Minimize instruction & control overhead
In-order core
SIMD (fp16 and fp8)
CISC instructions: up to 4D tensor operands
  Akin to DSP processors
  Issuing one instruction per cycle can keep all execution units busy
Temporal flexibility
Main thread & 8 threads
Switch to thread cycle-by-cycle when main thread waiting for data
Spatial: Near memory computing
Half of core is SRAM
SRAM
Compute + NoC

## Slide 44: Spatial Communication
Mesh NoC, 32b links
Explicit data movement (no global address)
24 virtual channels (colors) enable traffic multiplexing over links
Static switching: each router programmed with per-colour table
Somewhat like registered & multiplexed FPGA interconnect
S. Li, “Cerebras Architecture Deep Dive: First Look Inside the Hardware/Software Co-Design for Deep Learning, IEEE Micro, 2023.

## Slide 45: Streaming Dataflow Compute Model
Computation triggered by data arrival from NoC
Latency-insensitive communication
Output  local SRAM or NoC
Popular FPGA compute model, adapted to software-programmable cores
S. Li, “Cerebras Architecture Deep Dive: First Look Inside the Hardware/Software Co-Design for Deep Learning, IEEE Micro, 2023.

## Slide 46: Scale to Wafer
Within reticle: fabric uses parallel links with registers at routers
Reticle crossing: fewer wires  use source-synchronous interface that provides full bandwidth
Modest number of cycles to cross  fabric not interrupted by reticle boundaries
S. Li, “Cerebras Architecture Deep Dive: First Look Inside the Hardware/Software Co-Design for Deep Learning, IEEE Micro, 2023.

## Slide 47: Redundancy for Yield
Image: Sean Lie, “How Cerebras Solved the Yield Problem,” YouTube
Similar idea to Altera FPGAs, but details different
Redundant links to route around broken PEs
Invisible to Cerebras SW: it can assume a slightly smaller perfect array

## Slide 48: CAD Flow: Spatio-Temporal Mapping
Spatial: similarities to FPGA CAD
  Place 900,000 processors to minimize communication distance (wirelength) and latency (timing)
  Route traffic through mesh-based NoC
    Static routes; 24 colors per router
    Like an FPGA routing channel with 24 tracks
    But all time-domain multiplexed onto the same links
Temporal:
  Processors with local SRAM: temporal computation
  Can modify the ‘static’ routes over time  like partial reconfiguration

## Slide 49: Large Language Model (LLM) Inference on the WSE
Many cores allocated to each layer of an LLM
  Distributed matrix-vector multiplication, attention, …
Output token vector passes to next layer in a spatial pipeline
All weights stored on wafer  near-memory computing
Good match to auto-regressive LLM inference
S. Li, “Wafer-Scale AI: GPU Impossible Performance,” Hot Chips, 2024.

## Slide 50: Bigger Models  Pipeline Across WSEs
S. Li, “Wafer-Scale AI: GPU Impossible Performance,” Hot Chips, 2024.
Lower precisions benefit memory: fp8 weights  2x WSE-3

## Slide 51: Datacenter-Scale Up Comparison
Multiple Cerebras WSE networked  can form a pipeline
Hierarchical composition: NVL72 is 72 GPUs (144 dice) + 36 CPUs + custom NVLink interconnect
Networking can connect multiple NVL72

## Slide 52: LLM Inference Performance (GPT-OSS-120B)
https://www.cerebras.ai/blog/blackwell-vs-cerebras
Nov. 6, 2025
Tokens per second (each user): critical for reasoning models, large scale code generation, etc.
CGRA
Tokens / sec

## Slide 53: Wrap Up and Some Personal Lessons Learned

## Slide 54: CAD and Architecture Challenges
Spatial computing & more-than-moore well suited to DL
Don’t be too programmable  much of DL is repetitive matrix-vector and matrix-matrix ops
Custom SoCs with FPGA logic, die-stacked FPGAs, unique accelerators
  Have tools to investigate (e.g. VTR)
  Tools to implement (e.g. OpenFPGA)
  Era of bespoke FPGAs?
Wafer-scale and spatio-temporal computation
  Cerebras arch, AMD AI engines, …
  Complex mapping problem: spatial & temporal
  Need new architecture evaluation tools
  Huge space to explore: many discoveries to make!

## Slide 55: Personal Lessons Learned
Technical breadth is very useful
  I like learning how more things fit together
    Software, CAD, hardware, applications, more-than-Moore manufacturing, …
    Led to many of my biggest research and industrial successes
    And interesting!
Building to last / extend fits well with breadth
  VPR/VTR: has gone much farther than I ever expected
  Key was integrating features together, in a maintainable way