## Slide 1: Verilog to Routing (VTR): A Flexible Open-Source CAD Flow to Explore and Target Diverse FPGA Architectures
Vaughn Betz
With thanks to all VTR contributors, and particularly Kevin Murray for assistance in creating this presentation

## Slide 2: Agenda
FPGAs: Basics & Utility
Flexible CAD: Motivation and Challenges
Verilog to Routing: Recent Progress
    Architecture Generality
    AIR: Faster, More Adaptive Routing
    VTR 8.0: QoR Improvements
    Reinforcement Learning for Adaptive Placement
  Summary

## Slide 3: FPGA Basics & Utility

## Slide 4: FPGA Basics
Programmable Hardware
    Can implement arbitrary circuits
    Look-Up Table (LUT) implements logic
    Flip-Flop (FF) stores sequential state

## Slide 5: FPGA Basics
Logic Block (LB)
    Group of Logic Elements (LEs)
…

## Slide 6: FPGA Basics
Device
Grid of Function Blocks
Interconnect
IO
IO
IO
IO
RAM
RAM
RAM
RAM
DSP
DSP
DSP
DSP
LB
LB
LB
LB
LB
LB
LB
LB
LB
LB
LB
LB
LB
LB
LB
LB
LB
LB
LB
LB
Routing Switch

## Slide 7: FPGA Basics
Logic Synth.
Tech. Map
Pack
Place
Route
HDL
Bitstream
Mapping Applications to an FPGA
    Modern FPGAs are large (>10M LEs)
    Use Computer Aided Design (CAD) flow!
      Designer: provides behavioural specification
      Algorithms & tools: figure out the details

## Slide 8: Why Use an FPGA?
Flexible I/O
    No off-the-shelf chip with right I/O
Power Efficiency
    CPU/DSP/GPU performance per watt too low
Programmability
    Dedicated ASIC not practical (e.g. changing workload)
45 nm CPU energy breakdown [1]
0.03 pJ for 8-bit int add
0.90 pJ for 32-bit fp add
[1] M. Horowitz, “Computing’s Energy Problem,” ISSCC, 2014.

## Slide 9
  Widely Used Across Many Domains
  CAD flow key to success

## Slide 10: Flexible, Open Source CAD: Motivation and Challenges

## Slide 11: I: FPGA Architecture Research
Challenges:
Need representative benchmarks
Describe FPGA Architecture
Need high quality CAD flow
Benchmarks
FPGA Architecture #1
Speed/Area/
Power
FPGA Architecture #2
Speed/Area/
Power
Need CAD Flow for Architecture #1
Need CAD Flow for Architecture #2

## Slide 12: Why New FPGA Architectures?
Process Technology Changes
      Wire resistance, power limits, interposers, …
2. Application Changes
    New standards, faster processing: 4G  5G, …
    Deep Learning  new compute demands
    Embedded FPGAs
    3. Innovative Architecture Ideas!
(12)
Video
Vision
MEM
CPU
FPGA

## Slide 13: II: FPGA CAD Research
  New idea for CAD algorithm
  Need infrastructure!
    Do not build it all
    Focus on your contribution
  Common framework:
    Best practise
    Compare results
  Flexible CAD: more impact
    VTR enhancements help Symbiflow (QuickLogic EOS S3, Xilinx Artix7), start-ups, architecture research, …

## Slide 14: III: Program Novel Spatial Compute Architectures
  Have an architecture? Build it!
    FPGA/FPGA+???/???
    Need a CAD flow!
OpenFPGA (U of Utah) [2]
PRGA (Princeton) [3]
ReImagine: FPGA + Imager
(MIT Lincoln Lab) [1]
Custom FPGA
[1] https://www.darpa.mil/attachments/Final_Compiled_ReImagineProposersDay.pdf
[2] OpenFPGA: a Complete Open Source Frameworkfor FPGA Prototyping, Open Source Design Automation, 2019 (https://sites.google.com/site/pegaillardon/research/openfpga)
[3] PRGA: An Open-source Framework for Buildingand Using Custom FPGAs, Open Source Design Automation, 2019 (https://prga.readthedocs.io)

## Slide 15: VTR: Verilog to Routing

## Slide 16: Verilog to Routing (VTR) Project
Pack
Place
Route
Analysis
STA
Netlist
Verilog
VPR
ABC
ODIN II
Architecture
QoR
Open Source FPGA CAD Flow
Approach:
Architecture Agnostic
Data-driven FPGA Architecture description

## Slide 17: VTR Challenges
Architecture
Generality
Quality
Run-time
Can take hours to days (for large designs)
Accurate architecture conclusions
Reduces designer effort
Explore larger design space
Can we have all three?

## Slide 18: Outline
Pack
Place
Route
Analysis
STA
Netlist
Verilog
VPR
ABC
ODIN II
Architecture
QoR
1
2
3
4
VTR 8 Capabilities & New Features
1
AIR: Adaptive Incremental Router
2
VTR 8 QoR, Run-time & CAD Enhancements
3
Reinforcement Learning Enhanced Placement
4

## Slide 19: Outline
Pack
Place
Route
Analysis
STA
Netlist
Verilog
VPR
ABC
ODIN II
Architecture
QoR
1
2
3
4
VTR 8 Capabilities & New Features
1
AIR: Adaptive Incremental Router
2
VTR 8 QoR, Run-time & CAD Enhancements
3
Reinforcement Learning Enhanced Placement
4
K. E. Murray, et al., “VTR 8: High Performance CAD and Customizable FPGA Architecture Modelling", ACM TRETS, 2020

## Slide 20: Block Modeling
  Supports both soft & hard blocks
  Arbitrary:
    Netlist Primitives
    Hierarchy
    Connectivity
4-LUT
6-LUT
?
Logic Primitive
Logic Block Size
Inter-Element Connectivity
Logic Element
+

## Slide 21: General Device Grids
Perimeter
Fill
Column
Region
Single
New!

## Slide 22: Arbitrary Grid Example
Block RAM
IOs
DSP
Hard
Block
NoC
Router
Logic Block
New!

## Slide 23: Detailed Routing Architecture
Block Input Connection
Block Output Connection
Wire-Wire Connections
(switch-block)
Routing
Wires
Direct Block-Block Connection

## Slide 24: Customizable Routing Architectures
Switch-block Locations
Wire Connectivity
Non-Configurable Edges
New!
Notes: Custom SB: Oleg Petelin – data-driven architecture description
SB Locations: Large processor using all metal layers, shorted wires over hard block (e.g. RAM)
Non-config edges: Buffers (clock networks), L/T wires (Xilinx, Academic) – keep common case simple, elegant extension via non-configurable

## Slide 25: Fully Custom Routing Architectures
Pack
Place
Route
Analysis
STA
Netlist
Verilog
VPR
ABC
ODIN II
QoR
Arch.
RR
Graph
  Load RR graph from file
    VPR or non-VPR generated
  Full control of routing network
  Allows freezing RR graph (e.g. taped-out)
New!
Notes: Researchers & companies have taped out chips, used VTR as CAD system – must match chip!

## Slide 26: Analysis & Modeling
  Run analysis independent of optimization
  Improved visualizations & reporting
  Improved area models
  Full featured timing analysis
    Min & max timing models
    Multi-clock primitives
New & Enhanced!
Timing Reports
Routing Utilization
Critical Path
Multi-clock Primitives

## Slide 27: Outline
Pack
Place
Route
Analysis
STA
Netlist
Verilog
VPR
ABC
ODIN II
Architecture
QoR
1
2
3
4
VTR 8 Capabilities & New Features
1
AIR: Adaptive Incremental Router
2
VTR 8 QoR, Run-time & CAD Enhancements
3
Reinforcement Learning Enhanced Placement
4
K. E. Murray, et al., "AIR: A Fast but Lazy Timing-Driven FPGA Router", ASP-DAC, 2020, 1-7.

## Slide 28: FPGA Routing Problem
Model interconnect network as Routing Resource (RR) graph:
  Nodes: Conductors (wires/pins)
  Edges: Configurable switches
FPGA Routing Problem:
  Find embedding of netlist in RR graph
  Requires finding many non-overlapping trees in RR graph
  Minimize timing and wiring (power)
  Reasonable run-time
Usually solved as single combined global/detailed routing stage
Routing Resource (RR) Graph
Routing Architecture
Notes: Run-time: FPGAs have ‘instant’ manufacturing, makes CAD run-time very critical!

## Slide 29: Negotiated Congestion Routing
Net Router
nets
Connection Router
conns
Rip-up Nets
Increase Cong. Costs
Legal?
No
Yes
Done!
Re-route
Allow multiple nets to use same resources (congestion)
  Nets negotiate for resources
  Nets do not block each other
Congested!
Congestion Free!
Notes: Single stage:

## Slide 30: AIR: Adaptive Incremental Router
Negotiated congestion router
Adaptive Routing
Lazy Routing
Avoid unnecessary work!
Improve quality & robustness

## Slide 31: Connection Router: Architecture Adaptation
n
Base Resource Cost
Congestion Cost
Timing
Criticality
Net Router
nets
Connection Router
conns
Rip-up Nets
Increase Cong. Costs
Legal?
No
Yes
Done!
Re-route
S
t
  AIR uses adaptive:
  Lookahead:
  Base Costs : (see paper)

## Slide 32: Adaptive Lookahead
Observation: Lookahead should adapt to routing architecture
Classic Lookahead Delay
Map Lookahead Delay
Challenges:
  Many FPGA Architectures
  Huge Graph
  Reasonable build time
  Fast evaluation
Approach:
  Profile graph with un-directed Djikstra flood & automatically data reduce
  Adapts to graph
  More accurate → faster for equivalent/better quality
Lower delay

## Slide 33: Net Router: Lazy Routing
AIR Routes Nets Lazily:
Efficiently handle High-Fanout nets
Incrementally re-route congested nets
Net Router
nets
Connection Router
conns
Rip-up Nets
Increase Cong. Costs
Legal?
No
Yes
Done!
Re-route

## Slide 34: High-Fanout (HF) Routing
Observation: Most routing of HF net irrelevant for a particular sink
  But still consider as potential branch points (expensive)
Optimization:
  Only consider branch points spatially nearby target
  Don’t even look at others
  Limit search to region near target

## Slide 35: HF Router Expansion
Traditional
Spatial Lookup
Notes: Visualizing nodes explored (total cost) while routing HF net connection. Color proportional to cost.
Small neuron benchmark, ~3500 fanout net

## Slide 36: Incremental Routing
Observation: Most net connections routed legally
Optimization:
  Rip-up illegal sub-trees
  Re-route only those sub-tree connections
Challenge: May degrade critical path
  Fix: Also rip-up delay sub-optimal connections
A
B
D
G
H
F
C
E
A
B
D
G
H
F
C
I
A
B
D
G
H
F
C
Rip-up
Re-route

## Slide 37: Evaluation Titan Flow & Benchmarks
Pack
Place
Route
Analysis
STA
Netlist
Verilog
VPR
Quartus
Map
Quartus
Fit
QoR
QoR
Stratix IV Model
Titan Flow:
Synth. & Tech-Map with Quartus
Pack/Place/Route with Quartus or VPR
Titan Benchmarks:
Target Stratix IV
23 designs, 90K-1.9M primitives
Academic Routers:
  VPR 7
  CRoute
  AIR
Commercial Routers:
  Intel Quartus 18.0
Notes: Scott Whitty

## Slide 38: AIR Outperforms Academic Routers
Chart: Normalized Value
| Routed WL | Routed CPD | Route Time
AIR | 0.85 | 0.81 | 0.15
CRoute | 0.89 | 0.95 | 0.3
VPR 7 | 1 | 1 | 1
> 6.6x run-time reduction
Incr. Routing
HF Routing
Lookahead
19% faster critical path
Lookahead
15% less
wiring
Resource Base Costs
Lookahead
Notes: CRoute: Decomposes nets into indep. Connections
AIR: Incremental approach, still exploits net structure
Versus CROUTE:
2x run-time reduction
17% faster CPD
5% WL

## Slide 39: AIR is Faster than Quartus
Chart: Normalized Value
| Routed WL | Routed CPD | Route Time
VPR 8 Place + AIR Route | 1.27 | 1.23 | 0.23
Intel Quartus 18.0 | 1 | 1 | 1
Gap due to lower quality placement
4x run-time reduction

## Slide 40: AIR Effectively Resolves Congestion
Chart: Normalized Value
| Routed WL | Routed CPD
AIR Congestion Free (legal) | 0.86 | 1
AIR Congestion Oblivious (min. delay) | 1 | 1
Critical Path not degraded
Wiring reduced
Notes: Cong. Obliv: All connections timing critical, all get best timing, all use as much wire as needed
No change in CPD, 14% WL reduction (non-critical re-routed for WL)

## Slide 41: Outline
Pack
Place
Route
Analysis
STA
Netlist
Verilog
VPR
ABC
ODIN II
Architecture
QoR
1
2
3
4
VTR 8 Capabilities & New Features
1
AIR: Adaptive Incremental Router
2
VTR 8 QoR, Run-time & CAD Enhancements
3
Reinforcement Learning Enhanced Placement
4
K. E. Murray, et al., “VTR 8: High Performance CAD and Customizable FPGA Architecture Modelling", In submission to ACM TRETS, 2020

## Slide 42: Titan Benchmark Completion
Tool | Routed Benchmarks | Unroutable Benchmarks | Device Too Small
VTR 7 | 14 | 9 | -
VTR 8 | 23 | 0 | -
Quartus 18.0 | 20 | 1 | 2
VTR 8 Titan Benchmark Implementations

## Slide 43: Packing & Placement Enhancements
Avoid highly interconnected (unnatural) clusters
Avoid packing unrelated logic
Include more indirect (e.g. transitive) connectivity measures
De-prioritize high-fanout nets
Unclustered
Naturally Clustered
Clustered with Unrelated Logic
VTR 7
VTR 8
des90 Routing Utilization
Improved Placement Exploration
Better macro/carry-chain swapping
Improved swapping of sparse blocks

## Slide 44: VTR 8 Run-time & Memory Footprint
Chart: 
| Peak Memory | STA Time* | Total Time | Route Time | Place Time | Pack Time
 | 0.96 | 0.3 | 0.83 | 0.34 | 1 | 1.18
Quartus 18.0
7.2%
78.0%
9.8%
100.0%
2.4%
% Total
Run-time & memory comparable to commercial tools

## Slide 45: VTR 8 QoR
Chart: 
| Routed CPD (geomean) | Routed Wirelength | M144Ks | M9Ks | DSPs | LABs
 | 1.2 | 1.26 | 0.87 | 1.3 | 0.97 | 0.95
Quartus 18.0
Quality in the range of commercial tools

## Slide 46: Outline
Pack
Place
Route
Analysis
STA
Netlist
Verilog
VPR
ABC
ODIN II
Architecture
QoR
1
2
3
4
VTR 8 Capabilities & New Features
1
AIR: Adaptive Incremental Router
2
VTR 8 QoR, Run-time & CAD Enhancements
3
Reinforcement Learning Enhanced Placement
4
K. E. Murray and V. Betz, “Adaptive FPGA Placement Optimization via Reinforcement Learning", MLCAD, 2019

## Slide 47: Reinforcement Learning & CAD

## Slide 48: CAD Tool Development: Human-in-the-loop
  With human-in-the-loop:
  Slow
  Simple heuristics, limited tool parameters (to keep tractable)
  Tune for average case (can’t investigate every benchmark design)
Tool
Idea
Tune
Evaluate
  Large solution space → Use heuristics

## Slide 49: CAD Tool Development: Reinforcement Learning (RL)
  With RL:
  Human out of the loop!
  Learn better heuristics: exploit more information, more parameters
  Online adaptation → better than average case
Tool
Idea
Act
Reward
Learn
Tool
Notes: Not auto-tuner, can be deeper within the tool

## Slide 50: FPGA Placement

## Slide 51: Simulated Annealing (SA) Placement
  Modify placement by making ‘moves’
  Accept/Reject move based on:
    Cost change
    Temperature (hill climbing)
Logic
RAM
DSP

## Slide 52: Move Generation
Many possible types of moves!
Simple: random swap
Smart: directed move to ‘good’ location (wirelength, timing)
Complex: Analytic
Complex: Assignment
Many considerations:
  Frequencies of different moves
  Situation dependent?
  Move ‘strength’ vs run-time
Treat as RL Problem!
Notes: SA as framework for bucket of algorithms (SA as true meta-heuristic)
Situation dependent:
* Early/Late placement
* Circuit structure

## Slide 53: RL Move Generator
Actions: moved different block types
  Reward:
    Accepted: -Δcost
    Rejected: 0
Agent:
    Estimates value of actions
    Selects action to take
Action/Move
‘Agent’
Move Evaluation
Logic
RAM
DSP
Acc/Rej
Δcost

## Slide 54: Estimating Action Values
Move
  Values of action are not stationary!
Logic
RAM
DSP
Agent determines ‘good’ move types online!
Notes: Track with recency weighted average
Short time scale: : Forgetful (adaptive)
* automatically oscillates between working on CLB vs MULt vs RAM
* No manual CAD design needed! (figured it out itself, online!)

## Slide 55: Action Selection: Exploration vs Exploitation
  ε-greedy: Mostly greedy (exploit), occasionally random (explore)
    ε: fraction of exploratory moves
No exploration harms quality
Exploit to save run-time
Notes: Quality vs run-time at various epsilon (exploration fraction)
Can go surprising low on epsilon (not get stuck in local minima). Why? Move still randomized, forgetful agent will try something else if current greedy action stops yielding reward

## Slide 56: Quality/Run-time Comparison
VTR Benchmarks (10K-165K primitives), 3 seeds
VTR Default

## Slide 57: Quality/Run-time Comparison
VTR Benchmarks (10K-165K primitives), 3 seeds
moves per temp

## Slide 58: Quality/Run-time Comparison
VTR Benchmarks (10K-165K primitives), 3 seeds

## Slide 59: Quality/Run-time Comparison
VTR Benchmarks (10K-165K primitives), 3 seeds
20% faster
50% faster

## Slide 60: Conclusion
  RL-enhanced Simulated Annealing based FPGA Placer
    RL agent controlled move generator
    Learns on-line what types of moves are productive
    Improves run-time/quality trade-offs
      Particularly at low run-times
    Much more to explore
      More diverse placement perturbations / moves
      More powerful agents

## Slide 61: Summary

## Slide 62: Summary
  Open-source, flexible CAD crucial for
    Evolution/innovation in spatial hardware
    Enabling CAD research by the community
  VTR
    Large, very active open-source effort
      >12,000 commits, ~100 committers
    Linked to other open-source efforts like Symbiflow, OpenFPGA
      Mix and match your flow
    Flexible, with good (but can be better!) result quality
    Contributions welcome!
  Open source enables innovation across a wider community

## Slide 63: Thanks!
Questions? Email: vaughn@eecg.utoronto.ca
VTR: verilogtorouting.org