## Slide 1: ECE 454 Computer Systems Programming Memory performance (Part II: Optimizing for caches)
Ding Yuan
ECE Dept., University of Toronto
http://www.eecg.toronto.edu/~yuan

## Slide 2: Content
  Cache basics and organization (last lec.)
  Optimizing for Caches (this lec.)
    Tiling/blocking
    Loop reordering
  Prefetching (next lec.)
  Virtual Memory (next lec.)

## Slide 3: Optimizing for Caches

## Slide 4: Memory Optimizations
Write code that has locality
  Spatial: access data contiguously
  Temporal: make sure access to the same data is not too far apart in time
How to achieve?
  Proper choice of algorithm
  Loop transformations

## Slide 5: Background: Array Allocation
Basic Principle
  T A[L];
  Array of data type T and length L
  Contiguously allocated region of L * sizeof(T) bytes
char string[12];
x
x + 12
int val[5];
x
x + 4
x + 8
x + 12
x + 16
x + 20
double a[3];
x + 24
x
x + 8
x + 16
char *p[3];
x
x + 4
x + 8
x + 12

## Slide 6: Multidimensional (Nested) Arrays
Declaration
  T A[R][C];
  2D array of data type T
  R rows, C columns
  T element requires K bytes
Array Size
  R * C * K bytes
Arrangement
  Row-Major Ordering (C code)
A[0][0]
A[0][C-1]
A[R-1][0]
• • •
• • •
A[R-1][C-1]
•
•
•
•
•
•
int A[R][C];
• • •
A
[0]
[0]
A
[0]
[C-1]
• • •
A
[1]
[0]
A
[1]
[C-1]
• • •
A
[R-1]
[0]
A
[R-1]
[C-1]
• • •
4*R*C Bytes

## Slide 7: Assumed Simple Cache
2 ints per block
2-way set associative
2 blocks total
1 set
i.e., same thing as fully associative
Replacement policy: Least Recently Used (LRU)
Cache
Block 0
Block 1

## Slide 8: Some Key Questions
How many elements are there per block?
Does the data structure fit in the cache?
Do I re-use blocks over time?
In what order am I accessing blocks?

## Slide 9: Simple Array
1 | 2 | 3 | 4
A
Cache
for (i=0;i<N;i++){
… = A[i];
}
Miss rate = #misses / #accesses =
(N/2) / N = ½ = 50%

## Slide 10: Simple Array w outer loop
1 | 2 | 3 | 4
A
Cache
for (k=0;k<P;k++){
for (i=0;i<N;i++){
… = A[i];
}
}
Assume A[] fits in the cache:
Miss rate = #misses / #accesses =
(N/2) / N*P = 1/2P
Lesson: for sequential accesses with re-use,
If fits in the cache, first visit suffers all the misses

## Slide 11: Simple Array
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
A
Cache
for (i=0;i<N;i++){
… = A[i];
}
Assume A[] does not fit in the cache:
Miss rate = #misses / #accesses

## Slide 12: Simple Array
5 | 6
7 | 8
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
A
Cache
for (i=0;i<N;i++){
… = A[i];
}
Assume A[] does not fit in the cache:
Miss rate = #misses / #accesses = (N/2) / N = ½ = 50%
Lesson: for sequential accesses, if no-reuse it doesn’t
matter whether data structure fits

## Slide 13: Simple Array with outer loop
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
A
Cache
Assume A[] does not fit in the cache:
Miss rate = #misses / #accesses =
for (k=0;k<P;k++){
for (i=0;i<N;i++){
… = A[i];
}
}
(N/2) / N = ½ = 50%
Lesson: for sequential accesses with re-use,
If the data structure doesn’t fit,
same miss rate as no-reuse

## Slide 14: 2D array
A
Cache
Assume A[] fits in the cache:
Miss rate = #misses / #accesses =
for (i=0;i<N;i++){
for (j=0;j<N;j++){
… = A[i][j];
}
}
1 | 2
3 | 4
(N*N/2) / (N*N) = ½ = 50%

## Slide 15: 2D array
A
Cache
for (i=0;i<N;i++){
for (j=0;j<N;j++){
… = A[i][j];
}
}
Lesson: for 2D accesses, if row order and no-reuse,
same hit rate as sequential, whether fits or not
1 | 2 | 3 | 4
5 | 6 | 7 | 8
9 | 10 | 11 | 12
13 | 14 | 15 | 16
Assume A[] does not fit in the cache:
Miss rate = #misses / #accesses =
(N*N/2) / (N*N) = ½ = 50%

## Slide 16: 2D array
A
Cache
for (j=0;j<N;j++){
for (i=0;i<N;i++){
… = A[i][j];
}
}
Lesson: for 2D accesses, if column order and no-reuse,
same hit rate as sequential if entire column fits in the cache
1 | 2
3 | 4
Assume A[] fits in the cache:
Miss rate = #misses / #accesses = (N*N/2) / N*N = ½ = 50%

## Slide 17: 2D array
A
Cache
Assume A[] does not fit in the cache:
Miss rate = #misses / #accesses
1 | 2 | 3 | 4
5 | 6 | 7 | 8
9 | 10 | 11 | 12
13 | 14 | 15 | 16
for (j=0;j<N;j++){
for (i=0;i<N;i++){
… = A[i][j];
}
}
= N*N / N*N = 100%
Lesson: for 2D accesses, if column order, if entire column
doesn’t fit, then 100% miss rate (block (1,2) is gone
after access to element 9).

## Slide 18: 2 2D Arrays
A
Cache
A[] does not fit, B[] does not fit,
column of B[] does not fit (at same time as row of A[])
Miss rate = #misses / #accesses =
for (i=0;i<N;i++){
for (j=0;j<N;j++){
for (k=0;k<N;k++){
… = A[i][k] *
B[k][j];
}
}
1 | 2 | 3 | 4
5 | 6 | 7 | 8
9 | 10 | 11 | 12
13 | 14 | 15 | 16
B
17 | 18 | 19 | 20
21 | 22 | 23 | 24
25 | 26 | 27 | 28
29 | 30 | 31 | 32

## Slide 19: 2 2D Arrays
A
Cache
A[] does not fit, B[] does not fit,
column of B[] does not fit (at same time as row of A[])
Miss rate = #misses / #accesses =
for (i=0;i<N;i++){
for (j=0;j<N;j++){
for (k=0;k<N;k++){
… = A[i][k] *
B[k][j];
}
}
1 | 2
17 | 18
21 | 22
3 | 4
1 | 2 | 3 | 4
5 | 6 | 7 | 8
9 | 10 | 11 | 12
13 | 14 | 15 | 16
B
17 | 18 | 19 | 20
21 | 22 | 23 | 24
25 | 26 | 27 | 28
29 | 30 | 31 | 32
The most inner loop (i=j=0):
A[0][0] * B[0][0], A[0][1] * B[1][0],
A[0][2] * B[2][0], A[0][3] * B[3][0]
1
time
stamp
2
3
X
4
5

## Slide 20: 2 2D Arrays
A
Cache
A[] does not fit, B[] does not fit,
column of B[] does not fit (at same time as row of A[])
Miss rate = #misses / #accesses =
for (i=0;i<N;i++){
for (j=0;j<N;j++){
for (k=0;k<N;k++){
… = A[i][k] *
B[k][j];
}
}
1 | 2
25 | 26
21 | 22
3 | 4
1 | 2 | 3 | 4
5 | 6 | 7 | 8
9 | 10 | 11 | 12
13 | 14 | 15 | 16
B
17 | 18 | 19 | 20
21 | 22 | 23 | 24
25 | 26 | 27 | 28
29 | 30 | 31 | 32
The most inner loop (i=j=0):
A[0][0] * B[0][0], A[0][1] * B[1][0],
A[0][2] * B[2][0], A[0][3] * B[3][0]
3
6
4
5
time
stamp
X
7

## Slide 21: 2 2D Arrays
A
Cache
A[] does not fit, B[] does not fit,
column of B[] does not fit (at same time as row of A[])
Miss rate = #misses / #accesses =
for (i=0;i<N;i++){
for (j=0;j<N;j++){
for (k=0;k<N;k++){
… = A[i][k] *
B[k][j];
}
}
29 | 30
25 | 26
21 | 22
3 | 4
1 | 2 | 3 | 4
5 | 6 | 7 | 8
9 | 10 | 11 | 12
13 | 14 | 15 | 16
B
17 | 18 | 19 | 20
21 | 22 | 23 | 24
25 | 26 | 27 | 28
29 | 30 | 31 | 32
The most inner loop (i=j=0):
A[0][0] * B[0][0], A[0][1] * B[1][0],
A[0][2] * B[2][0], A[0][3] * B[3][0]
8
6
4
7
time
stamp

## Slide 22: 2 2D Arrays
A
Cache
A[] does not fit, B[] does not fit,
column of B[] does not fit (at same time as row of A[])
Miss rate = #misses / #accesses =
for (i=0;i<N;i++){
for (j=0;j<N;j++){
for (k=0;k<N;k++){
… = A[i][k] *
B[k][j];
}
}
29 | 30
25 | 26
21 | 22
3 | 4
1 | 2 | 3 | 4
5 | 6 | 7 | 8
9 | 10 | 11 | 12
13 | 14 | 15 | 16
B
17 | 18 | 19 | 20
21 | 22 | 23 | 24
25 | 26 | 27 | 28
29 | 30 | 31 | 32
Next time: (i=0, j=1):
A[0][0] * B[0][1], A[0][1] * B[1][1],
A[0][2] * B[2][1], A[0][3] * B[3][1]
8
6
4
7
time
stamp

## Slide 23: 2 2D Arrays
A
Cache
A[] does not fit, B[] does not fit,
column of B[] does not fit (at same time as row of A[])
Miss rate = #misses / #accesses =
for (i=0;i<N;i++){
for (j=0;j<N;j++){
for (k=0;k<N;k++){
… = A[i][k] *
B[k][j];
}
}
29 | 30
25 | 26
1 | 2
3 | 4
1 | 2 | 3 | 4
5 | 6 | 7 | 8
9 | 10 | 11 | 12
13 | 14 | 15 | 16
B
17 | 18 | 19 | 20
21 | 22 | 23 | 24
25 | 26 | 27 | 28
29 | 30 | 31 | 32
Next time: (i=0, j=1):
A[0][0] * B[0][1], A[0][1] * B[1][1],
A[0][2] * B[2][1], A[0][3] * B[3][1]
8
6
9
7
time
stamp

## Slide 24: 2 2D Arrays
A
Cache
A[] does not fit, B[] does not fit,
column of B[] does not fit (at same time as row of A[])
Miss rate = #misses / #accesses =
for (i=0;i<N;i++){
for (j=0;j<N;j++){
for (k=0;k<N;k++){
… = A[i][k] *
B[k][j];
}
}
29 | 30
17 | 18
1 | 2
3 | 4
1 | 2 | 3 | 4
5 | 6 | 7 | 8
9 | 10 | 11 | 12
13 | 14 | 15 | 16
B
17 | 18 | 19 | 20
21 | 22 | 23 | 24
25 | 26 | 27 | 28
29 | 30 | 31 | 32
Next time: (i=0, j=1):
A[0][0] * B[0][1], A[0][1] * B[1][1],
A[0][2] * B[2][1], A[0][3] * B[3][1]
8
10
9
7
time
stamp
X
11

## Slide 25: 2 2D Arrays
A
Cache
A[] does not fit, B[] does not fit,
column of B[] does not fit (at same time as row of A[])
Miss rate = #misses / #accesses =
for (i=0;i<N;i++){
for (j=0;j<N;j++){
for (k=0;k<N;k++){
… = A[i][k] *
B[k][j];
}
}
29 | 30
17 | 18
1 | 2
21 | 22
1 | 2 | 3 | 4
5 | 6 | 7 | 8
9 | 10 | 11 | 12
13 | 14 | 15 | 16
B
17 | 18 | 19 | 20
21 | 22 | 23 | 24
25 | 26 | 27 | 28
29 | 30 | 31 | 32
Next time: (i=0, j=1):
A[0][0] * B[0][1], A[0][1] * B[1][1],
A[0][2] * B[2][1], A[0][3] * B[3][1]
8
10
11
12
time
stamp

## Slide 26: 2 2D Arrays
A
Cache
A[] does not fit, B[] does not fit,
column of B[] does not fit (at same time as row of A[])
Miss rate = #misses / #accesses =
for (i=0;i<N;i++){
for (j=0;j<N;j++){
for (k=0;k<N;k++){
… = A[i][k] *
B[k][j];
}
}
3 | 4
17 | 18
1 | 2
21 | 22
1 | 2 | 3 | 4
5 | 6 | 7 | 8
9 | 10 | 11 | 12
13 | 14 | 15 | 16
B
17 | 18 | 19 | 20
21 | 22 | 23 | 24
25 | 26 | 27 | 28
29 | 30 | 31 | 32
Next time: (i=0, j=1):
A[0][0] * B[0][1], A[0][1] * B[1][1],
A[0][2] * B[2][1], A[0][3] * B[3][1]
13
10
11
12
time
stamp

## Slide 27: 2 2D Arrays
A
Cache
A[] does not fit, B[] does not fit,
column of B[] does not fit (at same time as row of A[])
Miss rate = #misses / #accesses =
for (i=0;i<N;i++){
for (j=0;j<N;j++){
for (k=0;k<N;k++){
… = A[i][k] *
B[k][j];
}
}
3 | 4
25 | 26
1 | 2
21 | 22
1 | 2 | 3 | 4
5 | 6 | 7 | 8
9 | 10 | 11 | 12
13 | 14 | 15 | 16
B
17 | 18 | 19 | 20
21 | 22 | 23 | 24
25 | 26 | 27 | 28
29 | 30 | 31 | 32
Next time: (i=0, j=1):
A[0][0] * B[0][1], A[0][1] * B[1][1],
A[0][2] * B[2][1], A[0][3] * B[3][1]
13
14
11
12
time
stamp
X
15

## Slide 28: 2 2D Arrays
A
Cache
A[] does not fit, B[] does not fit,
column of B[] does not fit (at same time as row of A[])
Miss rate = #misses / #accesses =
for (i=0;i<N;i++){
for (j=0;j<N;j++){
for (k=0;k<N;k++){
… = A[i][k] *
B[k][j];
}
}
3 | 4
25 | 26
29 | 30
21 | 22
1 | 2 | 3 | 4
5 | 6 | 7 | 8
9 | 10 | 11 | 12
13 | 14 | 15 | 16
B
17 | 18 | 19 | 20
21 | 22 | 23 | 24
25 | 26 | 27 | 28
29 | 30 | 31 | 32
Next time: (i=0, j=1):
A[0][0] * B[0][1], A[0][1] * B[1][1],
A[0][2] * B[2][1], A[0][3] * B[3][1]
15
14
16
12
time
stamp
75%

## Slide 29: Example: Matrix Multiplication
a
b
i
j
*
c
+=
c = (double *) calloc(sizeof(double), n*n);
/* Multiply n x n matrices a and b */
void mmm(double *a, double *b, double *c, int n) {
int i, j, k;
for (i = 0; i < n; i++)
for (j = 0; j < n; j++)
for (k = 0; k < n; k++)
c[i][j] += a[i][k]*b[k][j];
}

## Slide 30: Cache Miss Analysis
Assume:
  Matrix elements are doubles
  Cache block 64B = 8 doubles
  Cache capacity << n (much smaller than n)
    i.e., can’t even hold an entire row in the cache!
First iteration:
  How many misses?
  in cache at end of
  first iteration:
*
+=
*
+=
n/8 misses
n misses
  n/8 + n = 9n/8 misses
8 wide
8 wide

## Slide 31: Cache Miss Analysis
Assume:
  Matrix elements are doubles
  Cache block = 8 doubles
  Cache capacity << n (much smaller than n)
Second iteration:
  Number of misses: n/8 + n = 9n/8 misses
Total misses (entire mmm):
  9n/8 * n2 = (9/8) * n3
*
+=
8 wide
8 wide

## Slide 32: Doing Better
MMM has lots of re-use:
  try to use all of a cache block once loaded
Challenge
  we need both rows and columns to work with
Compromise:
  operate in sub-squares of the matrices
  One sub-square per matrix should fit in cache simultaneously
  Heavily re-use the sub-squares before loading new ones
  Called ‘Tiling’ or ‘Blocking’
    A sub-square is a ‘tile’

## Slide 33: Illustration
*
+=
*
+=
No tiling
Tiling

## Slide 34: Tiled Matrix Multiplication
c = (double *) calloc(sizeof(double), n*n);
/* Multiply n x n matrices a and b */
void mmm(double *a, double *b, double *c, int n) {
int i, j, k;
for (i = 0; i < n; i+=T)
for (j = 0; j < n; j+=T)
for (k = 0; k < n; k+=T)
/* T x T mini matrix multiplications */
for (i1 = i; i1 < i+T; i1++)
for (j1 = j; j1 < j+T; j1++)
for (k1 = k; k1 < k+T; k1++)
c[i1][j1] += a[i1][k1]*b[k1][j1];
}
a
b
i1
j1
*
c
+=
Tile size T x T

## Slide 35: Detailed Visualization
a
*
+=
b
c
Still have to access b[] column-wise
But now b’s cache blocks don’t get replaced

## Slide 36: Big picture
*
+=
First calculate C[0][0] – C[T-1][T-1]

## Slide 37: Big picture
*
+=
Next calculate C[0][T] – C[T-1][2T-1]
Notes: Note, the tile of A and B later will be evicted and re-fetched on other elements.

## Slide 38: Cache Miss Analysis
Assume:
  Cache block = 8 doubles
  Cache capacity << n (much smaller than n)
  Need to fit 3 tiles in cache: hence ensure 3T2 < capacity
    (since 3 arrays a,b,c)
Misses per tile-iteration:
  T2/8 misses for each tile
  2n/T * T2/8 = nT/4
Total misses:
  Tiled: nT/4 * (n/T)2 = n3/(4T)
  Untiled: (9/8) * n3
*
+=
Tile size T x T
n/T tiles