## Slide 1: ECE 454 Computer Systems Programming Parallel Architectures and Performance Implications (II)
Ding Yuan
ECE Dept., University of Toronto
http://www.eecg.toronto.edu/~yuan

## Slide 2: Putting it all together [1]
Performance implications for parallel architecture
Background: architecture of the two testing machines
Cache-coherence performance and implications to parallel software design
[1] Everything you always wanted to know about synchronization
but were afraid to ask. David, et. al., SOSP’13

## Slide 3: Two case studies
48-core AMD Opteron
80-core Intel Xeon

## Slide 4: 48-core AMD Opteron
RAM
LLC NOT shared
Directory-based cache coherence
(motherboard)
L1
C
L1
C
Last Level Cache
6-cores per die
L1
C
…6x…
…8x…
L1
C
L1
C
Last Level Cache
6-cores per die
L1
C
…6x…
cross-socket!

## Slide 5: 80-core Intel Xeon
RAM
LLC shared
Snooping-based cache coherence
(motherboard)
L1
C
L1
C
Last Level Cache
10-cores per die
L1
C
…10x…
…8x…
L1
C
L1
C
10-cores per die
L1
C
…10x…
cross-socket

## Slide 6: Interconnect between sockets
Cross-sockets communication can be 2-hops

## Slide 7: Performance of memory operations

## Slide 8: Local caches and memory latencies
Memory access to a line cached locally (cycles)
  Best case: L1 < 10 cycles
  Worst case: RAM 136 – 355 cycles

## Slide 9: Latency of remote access: read (cycles)
Ignore
“State” is the MESI state of a cache line in a remote cache.
Cross-socket communication is expensive!
  Xeon: loading from Shared state is 7.5 times more expensive over two hops than within socket
  Opteron: cross-socket latency even larger than RAM
Opteron: uniform latency regardless of the cache state
  Directory-based protocol
Xeon: load from “Shared” state is much faster than from “M” and “E” states
  “Shared” state read is served from LLC instead from remote cache

## Slide 10: Latency of remote access: write (cycles)
“State” is the MESI state of a cache line in a remote cache.
Cross-socket communication is expensive!
Opteron: store to “Shared” cache line is much more expensive
  Directory-based protocol is incomplete
    Does not keep track of the sharers
    Equivalent to broad-cast and have to wait for all invalidations to complete
Xeon: store latency similar regardless of the previous cache line state
  Snooping-based coherence
Ignore

## Slide 11: How about synchronization?

## Slide 12: Synchronization implementation
Hardware support is required to implement sync. primitives
  In the form of atomic instructions
  Common examples include: test-and-set, compare-and-swap, etc.
  Used to implement high-level synchronization primitives
    e.g., lock/unlock, semaphores, barriers, cond. var., etc.
  We will only discuss test-and-set

## Slide 13: Test-And-Set
The semantics of test-and-set are:
  Record the old value
  Set the value to TRUE
    This is a write!
  Return the old value
Hardware executes it atomically!
When executing test-and-set on “flag”
  What is value of flag afterwards if it was initially False? True?
  What is the return result if flag was initially False? True?
bool test_and_set (bool *flag){
bool old = *flag;
*flag = True;
return old;
}
Read-exclusive (invalidations)
Modify (change state)
Memory barrier
  completes all the mem. op.
  before this TAS
  cancel all the mem. op.
  after this TAS
Hardware implementation:
atomic!

## Slide 14: Using Test-And-Set
Here is our lock implementation with test-and-set:
When will the while return? What is the value of held?
Does it work? What about multiprocessors?
struct lock {
int held = 0;
}
void acquire (lock) {
while (test-and-set(&lock->held));
}
void release (lock) {
lock->held = 0;
}

## Slide 15: TAS and cache coherence
Shared Memory (lock->held = 0)
Cache
Processor
State
Data
Thread A:
Cache
Processor
State
Data
Thread B:
acquire(lock)
Read-Exclusive

## Slide 16: TAS and cache coherence
Shared Memory (lock->held = 0)
Cache
Processor
Dirty
State
lock->held=1
Data
Thread A:
Cache
Processor
State
Data
Thread B:
acquire(lock)
Read-Exclusive
Fill

## Slide 17: TAS and cache coherence
Shared Memory (lock->held = 0)
Cache
Processor
Dirty
State
lock->held=1
Data
Thread A:
Cache
Processor
acquire(lock)
State
Data
Thread B:
acquire(lock)
Read-Exclusive
invalidation

## Slide 18: TAS and cache coherence
Shared Memory (lock->held = 1)
Cache
Processor
Invalid
State
lock->held=1
Data
Thread A:
Cache
Processor
acquire(lock)
State
Data
Thread B:
acquire(lock)
Read-Exclusive
invalidation
update

## Slide 19: TAS and cache coherence
Shared Memory (lock->held = 1)
Cache
Processor
Invalid
State
lock->held=1
Data
Thread A:
Cache
Processor
acquire(lock)
Dirty
State
Data
Thread B:
lock->held=1
acquire(lock)
Read-Exclusive
Fill

## Slide 20: What if there are contentions?
Shared Memory (lock->held = 1)
Cache
Processor
State
Data
Thread A:
Cache
Processor
while(TAS(lock))
;
State
Data
Thread B:
while(TAS(lock))
;

## Slide 21: How bad can it be?
TAS
Recall: TAS essentially is a Store + Memory Barrier
Ignore
Store

## Slide 22: How to optimize?
When the lock is being held, a contending “acquire” keeps modifying the lock var. to 1
  Not necessary!
void test_and_test_and_set (lock) {
do {
while (lock->held == 1)
; // spin
}
} while (test_and_set(lock->held));
}
void release (lock) {
lock->held = 0;
}

## Slide 23: What if there are contentions?
Shared Memory (lock->held = 0)
Cache
Processor
Dirty
State
lock->held=1
Data
Thread A:
Cache
Processor
while(lock->held==1)
;
State
Data
Thread B:
holding lock
Cache
Processor
State
Data
Thread B:
Read
Read request

## Slide 24: What if there are contentions?
Shared Memory (lock->held = 1)
Cache
Processor
Shared
State
lock->held=1
Data
Thread A:
Cache
Processor
while(lock->held==1)
;
Shared
State
Data
Thread B:
lock->held=1
holding lock
Cache
Processor
State
Data
Thread B:
Read
Read request
update

## Slide 25: What if there are contentions?
Shared Memory (lock->held = 1)
Cache
Processor
Shared
State
lock->held=1
Data
Thread A:
Cache
Processor
while(lock->held==1)
;
Shared
State
Data
Thread B:
lock->held=1
holding lock
Cache
Processor
Shared
State
Data
Thread B:
lock->held=1
while(lock->held==1)
;
Repeated read to “Shared” cache line: no cache coherence traffic!

## Slide 26: Let’s put everything together
TAS
Load
Ignore
Write
Local access

## Slide 27: Implications to programmers
Cache coherence is expensive (more than you thought)
  Avoid unnecessary sharing (e.g., false sharing)
    Avoid unnecessary coherence (e.g., TAS -> TATAS)
  Clear understanding of the performance
Crossing sockets is a killer
  Can be slower than running the same program on single core!
  pthread provides CPU affinity mask
    pin cooperative threads on cores within the same die
Loads and stores can be as expensive as atomic operations
Programming gurus understand the hardware
  So do you!